## Slide 1: USDA APHIS LABORATORY ERGONOMICS

## Slide 2: Menu
Title Slide
Welcome – Role of APHIS
Successful Workplace
Objectives
Ergonomics Defined
Ergonomics Principles
  Neutral Position and Support
  Reach Zone
  Power Position
  Fatigue Control
WMSDs
Warm-up and Stretching
Physical Fitness Health/Wellness
Ergonomics Workstation Assessment
Workbenches, Stools and Footrests
Pipetting
Microscopy
Biological Safety Cabinets
Test Tube Handling
Material and Equipment Handling
Power Lift Technique
Available Services
Summary and Close
Resources

## Slide 3: Welcome to USDA APHIS Laboratory Ergonomics
Audio
Speaker icon on the left controls the audio (Play, Pause and Volume)
Handouts
Click on the icon to the right of the title to open the document
USDA APHIS Laboratory Ergonomics Assessment Worksheet
USDA APHIS Laboratory Ergonomics Tips
Stretching Poster
USDA APHIS Laboratory Questions
Notes: Hello everyone. Welcome to USDA APHIS Laboratory Ergonomics.
Click on the Menu link to access the Menu.
The Speaker Icon in the upper left corner controls the audio playback (play, pause and volume).
Handouts are available for the presentation and can be accessed by clicking on the icon to the right of the title.

## Slide 4: Role of APHIS
Multi-faceted Agency
  Protecting and promoting U.S. agricultural health
  Regulating genetically engineered organisms
  Administering Animal Welfare Act
Overall USDA mission
  Protect and promote food, agriculture, natural resources and related issues
Notes: The Animal and Plant Health Inspection Service is a multi-faceted Agency with a broad mission that includes protecting and promoting U.S. agricultural health, regulating genetically engineered organisms, administering the Animal Welfare Act and carrying out wildlife damage management activities.
These efforts support the overall mission of USDA, which is to protect and promote food, agriculture, natural resources and related issues.

## Slide 5: Work in APHIS Labs
Critical work in APHIS laboratories around United States
Training session details how to perform laboratory tasks
  Enhance agency’s mission
  Facilitate well-being and performance
  Application of ergonomics principles
Notes: A significant portion of this critical work takes place in APHIS laboratories around the United States.
In this training session we’ll detail how you can perform laboratory tasks that enhance the agency’s mission and facilitate your well-being and performance by the application of ergonomics principles and measures.

## Slide 6: Successful Workplace?
Expect to accomplish?
Words describe successful workplace?
Want a workplace that is
______________________
What do you think?
Notes: First though, what can you expect to accomplish from this training session?
Think for a moment, what words would you use to describe the successful workplace?
You want a workplace that is . . . ., well, fill in the blank. What do you think?

## Slide 7: First Word?
If you answered, “Comfortable” you’re not alone
About 9 out of 10 people
Then words like
  Productive
  Well-organized
  Functional
  Well lit
  Safe
Notes: Was the first word that came to your mind: “comfortable”?
If you answered, “comfortable”, you’re not alone.
Informal surveys indicate for about 9 out of 10 people “comfortable” is what they want in their workplace.
Then of course, words like “productive”, “well-organized”, “functional”, “well lit”, “safe” and so on follow along.

## Slide 8: Direct Relationship
Between workplace comfort levels and other descriptors
Workplace more comfortable is also more
  Productive
  Functional
  Safe
Use ergonomics principles and techniques
  Enhance comfort level
  Enhance safety and productivity
Notes: We recognize there is a direct relationship between workplace comfort levels and these other descriptors; a workplace that is more comfortable is typically also more productive, functional and safe.
That’s what this training session is all about; how you can use ergonomics principles and techniques in the lab environment to help you enhance your comfort level as well enhance your safety and productivity.

## Slide 9: Question on Successful Workplace
There is no relationship between an individual’s comfort level in the workplace and enhancing safety and productivity. True/False
Notes: Take a moment and answer the question. The answer is found on the next slide.

## Slide 10: Question on Successful Workplace
There is no relationship between an individual’s comfort level in the workplace and enhancing safety and productivity. True/False
Notes: Please go back and review the information if you missed the question.

## Slide 11: Objectives
Practical definition of ergonomics
Ergonomics principles
Common laboratory work-related musculoskeletal disorders (WMSDs)
Step-by-step ergonomics workstation assessment process
  Pipetting, microscopy
  Biological safety cabinets
  Set-up workstations
Notes: Specifically, you’ll learn a practical definition of ergonomics, ergonomics principles, and known common laboratory work-related musculoskeletal disorders (WMSDs) that may occur.
Most importantly, you will learn how to apply a step-by-step ergonomics workstation assessment process to laboratory tasks including pipetting, microscopy, use of biological safety cabinets and the set-up of laboratory workstations.

## Slide 12: Objectives
Personal performance and comfort
  Warmup and stretching
  Physical fitness
  Health and wellness
Apply this assessment process to other work or even home environments
Notes: We’ll also discuss specific strategies to enhance personal performance and comfort through warmup and stretching activities, physical fitness, and health and wellness activities.
As an additional benefit, people who have attended ergonomics sessions discover they can apply this assessment process to other work or even home environments.

## Slide 13: Ergonomics - Definition
Heard word, “ergonomics” before
Marketeers tout product’s “ergonomic” qualities and benefits
  Tool with “ergonomic” handle
  Car seat with “ergonomic design”
In lab environment how best to define ergonomics?
Any product illustrations do not constitute official USDA endorsement.
Notes: More than likely you have heard the word, “ergonomics” before.
It seems everywhere you look; marketeers are using the word to tout a product’s “ergonomic” qualities and benefits; a tool with an “ergonomic” handle or a car seat with “ergonomic design”.
Well, in the lab environment how do we best define ergonomics?

## Slide 14: Fit the Job to the Person
Very diverse workforce
Accommodate diverse population
  “Fit the job to the person.”
  Not force, “The person to fit the job.”
Microscopy
  Properly set-up for shorter person
  Very uncomfortable for taller person
  Potentially lead to musculoskeletal issue
Notes: Picture for a moment those who work in labs. Some are taller, some are shorter, some are smaller, and some are larger. In other words, just in terms of size there is a very diverse workforce.
Our challenge is to have a workplace that can accommodate this diverse population. In other words, we want to, “Fit the job to the person.”
This is in direct contrast to forcing, “The person to fit the job.”
A great example is microscopy.
A microscope properly set-up for a shorter person will be very uncomfortable for a taller person and can potentially lead to a musculoskeletal issue.

## Slide 15: Work Smarter, Not Harder
Control level of physical stress and exertion
Examine how tasks are accomplished
Develop methods to optimize performance
Notes: Another common definition of ergonomics involves controlling the level of physical stress and exertion required to perform the task at hand.
Here, the goal is to figure out methods to control the physical stresses and exertions by examining how tasks are accomplished and then develop methods to optimize performing the tasks.
The expression, “Work smarter, not harder” nicely sums up this concept.
So, our objective is to use the ergonomics assessment process to identify potential risk factors and then craft reasonable and viable methods to better, “Fit the Job to the Person” and “Work Smarter, Not Harder”.

## Slide 16: Ergonomics Principles
Neutral Position and Support
Reach Zone
Power Position
Fatigue Control
Ergonomics
Neutral Position
Reach Zone
Power Position
Fatigue Control
Notes: To help ensure the workplace is the most comfortable and effective possible, we’ll define a set of ergonomics principles.
We’ll focus on four of them:
Neutral Position and Support
Reach Zone
Power Position and
Fatigue Control

## Slide 17: Neutral Position and Support
Spine and pelvis provide foundation
S-shape configuration
  Inner curve in lower back and neck
  Outer curve in mid-back area
Why S-shape?
  Think springs!
Notes: The first ergonomics principle is Neutral Position and Support.
Although we stand upright on our feet, it's really the spine and pelvis that provide the foundation for our body.
When you hold yourself in the neutral position, your spinal column, when viewed from the side, is actually in an S-shape configuration.
An inner curve in the lower back and neck and an outer curve in the mid-back area.
Why S-shape? Think springs! The S-shape allows the spine to act like a spring and increases the spine’s ability to handle stress.

## Slide 18: Mid-range of Joint Position
What position of elbow most functional?
  With elbow straight or bent all the way?
About 90 degrees of bend
  Greatest strength
  Protects joint and surrounding soft tissues
Every joint of body has a “mid-range of joint position”
Notes: What about the other joints of the body? Every joint has a neutral position. We call it, “mid-range of joint position”.
Think about your elbow. From a physical performance standpoint, what position of the elbow is the most functional?
With the elbow straight or bent all the way?
The elbow is most functional at about 90 degrees of bend. This is the position of greatest strength and also protects the joint and surrounding soft tissues like muscles, tendons, ligaments and nerves.
Every joint of the body has a “mid-range of joint position”.

## Slide 19: Absolute Neutral Position
Can’t spend all time in neutral position
Next time in an out-of-neutral position
  Identify why out of neutral, consider options to improve
  15% can make a big difference
Notes: Of course, you can’t spend all your time with your spine and joints in the absolute neutral position.
However, the closer you can position your joints to the “mid-range of joint position”, the better.
The next time you find yourself in an out-of-neutral position, identify why you are out of neutral and consider options to improve the situation to allow you to be more in neutral.
Even if you can spend 15% more time in neutral, that 15% can make a big difference!
We’ll make use of the Neutral Position concept in assessing and setting up lab workstations and equipment.

## Slide 20: Reach Zone
How long hold 10# load at arm’s length?
  Gets heavy quite quickly
  Hold as close to your body as you can
Operating range
  Determined by arm’s length
  Sphere from hip to shoulder level within arm’s reach to the front and side
Notes: Reach Zone is the second ergonomics principle; it has to do with how far away from your body you need to reach.
For example, how long can you hold a 10# load at arm’s length?
Well, at arm's length, it gets heavy quite quickly.
That’s why, in fact, if you must hold the load at all, you know you want to hold it as close to your body as you can.
Structurally, the body is designed to function within a specific operating range. We call this the Reach Zone.
Determined by your arm’s length, it’s defined by a sphere from hip to shoulder level within arm’s reach to the front and side.

## Slide 21: Never Reach Outside Reach Zone?
Of course, the answer is NO!
Find yourself
  Reaching way outside reach zone
  Heavy load
  Awkward position
Set up to work within your Reach Zone
Notes: Are we saying never reach outside your reach zone? Of course, the answer is NO!
But if you find yourself reaching way outside your reach zone with a heavy load in an awkward position think about ways to decrease the reach distance.
In general, set up as much as possible to work within your Reach Zone. We’ll examine specific lab related situations a little later in the session.

## Slide 22: Power Position
Lift or move supplies, containers and equipment?
Neutral Position best position?
  As it turns out – it’s not
Power Position is better
Notes: So far, we have outlined the ergonomics principle of Neutral Position and Support and Reach Zone.
But what about if you have to lift or move supplies, containers and equipment?
Is the Neutral Position really the best position for this kind of activity?
As it turns out – it’s not.
From the body’s perspective the third ergonomics principle, Power Position is a better way to go.

## Slide 23: Power Position Looks Like:
Feet shoulder width or slightly wider
Good footing so you don’t slip
Spine maintained in neutral
Hips and knees bent slightly
Head and shoulders upright
Notes: Here’s what the Power Position looks like:
Feet shoulder width or slightly wider.
Good footing so you don’t slip.
Spine maintained in neutral.
Hips and knees bent slightly.
Head and shoulders upright.

## Slide 24: Ready” Position in Sports
Ready position in sports
Use Power Position
  Lifting materials
  Using tools and equipment
  Setting up the work area
Water fountain
  Give it a try!
Notes: In fact, this position is used in just about any sport as a “ready” position.
We’ll examine how you can use the Power Position in many ways – lifting materials but also, for using tools and equipment and setting up the work area.
You can even use the power position to get a drink at the water fountain! Rather than just bending over at the waist with your knees straight – stressing your lower back – use the power position.
Give it a try!

## Slide 25: Fatigue Control
“Control” and not “Eliminate”
Physical fatigue is normal occurrence
  Not possible to eliminate fatigue
For overall health and wellness
  Recover from fatigue through appropriate rest, hydration and nutrition
Notes: So far, we have gone over the ergonomics principles of Neutral Position and Support, Reach Zone and Power Position.
The last principle is Fatigue Control.
You’ll notice we’re using the word “Control” and not “Eliminate” when discussing fatigue.
Physical fatigue is a normal occurrence in the routine of our lives. It is not possible to eliminate fatigue.
For overall health and wellness, we need to recover from fatigue through appropriate rest, hydration and nutrition.

## Slide 26: Recognize Fatigue?
Physical and/or repetitive tasks result in muscle tiredness
Decrease in general physical strength and coordination
More prone to making mistakes
More likely to experience injuries
Notes: First, how do you recognize fatigue? Physical fatigue is demonstrated when physical and/or repetitive tasks result in muscle tiredness.
We experience a decrease in general physical strength and coordination.
We are more prone to making mistakes.
We may be more likely to experience injuries.

## Slide 27: What Can You Do to Control Fatigue?
Mix up job tasks to provide variety of physical activities
Break a larger task into smaller tasks
  Alternate lab tasks, like pipetting between right and left hands
Appropriate recovery breaks
  Replenish energy supplies and fluid intake
  Try to not skip breaks and lunch
Notes: What can you do to control fatigue?
Try to mix up job tasks to provide a variety of physical activities. This is called job rotation. Break a larger task into smaller tasks.
For example, when possible alternate lab tasks, like pipetting between right and left hands.
Make sure you take appropriate recovery breaks to give your body a chance to replenish energy supplies and fluid intake.
In other words, try to not skip breaks and lunch.

## Slide 28: What Can You Do to Control Fatigue?
Drink plenty of fluid on a periodic basis
Stretching
  Promote blood circulation and joint lubrication
Consciously work to identify and control fatigue at work!
Notes: Drink plenty of fluid on a periodic basis. If you are thirsty you are on your way to dehydration.
Use stretching to promote blood circulation and joint lubrication.
Look at the Physical Fitness, Health and Wellness and Stretching sections for details about using stretching as a part of your overall fatigue control strategy.
Consciously work to identify and control fatigue at work.

## Slide 29: Use Ergonomics Principles
Ergonomics is all about fitting job to the person and working smarter not harder
Four ergonomics principles
  Neutral Position and Support
  Reach Zone
  Power Position
  Fatigue Control
Help guide how to safely and effectively do your work
Notes: So, ergonomics is all about fitting the job to the person and working smarter not harder.
We’ve discussed four ergonomics principles:
Neutral Position and Support
Reach Zone
Power Position and
Fatigue Control
You can use these principles to help guide how to safely and effectively do your work. Check out the Tips and Techniques Section for additional examples.

## Slide 30: Questions on Ergonomics
Ergonomics can be defined as:
Fitting the job to the person.
Fitting the person to the job.
Working harder, not smarter.
Working smarter, not harder.
A and D
Basic ergonomics principles include:
Neutral Position and Support
Reach Zone
Power Position
Fatigue Control
All of the above
The feet are considered to be the foundation of the body. True/False
When viewed from the side, the spinal column in the Neutral Position:
Has a C-shape.
Has three curves.
Is a straight column
Mid-range of joint position for the body’s joints:
Is the weakest position of the joint.
Is the most functional position of the joint.
Can be maintained 100% of the time.
As possible it makes sense to set-up your workstation within your Reach Zone. True/False
The Power Position:
Is a “ready” position for almost every sport.
Can be used when lifting a box.
Can be used when getting a drink at the water fountain.
All of the above.
It is possible to eliminate fatigue from our day-to-day activities. True/False
Ideas to control fatigue include:
Alternating job tasks throughout the day.
Taking appropriate recovery breaks
Maintaining adequate hydration.
Using stretching as “microbreaks”.
All of the above.
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 31: Questions on Ergonomics
Ergonomics can be defined as:
Fitting the job to the person.
Fitting the person to the job.
Working harder, not smarter.
Working smarter, not harder.
A and D
Basic ergonomics principles include:
Neutral Position and Support
Reach Zone
Power Position
Fatigue Control
All of the above
The feet are considered to be the foundation of the body. True/False
When viewed from the side, the spinal column in the Neutral Position:
Has a C-shape.
Has three curves.
Is a straight column
Mid-range of joint position for the body’s joints:
Is the weakest position of the joint.
Is the most functional position of the joint.
Can be maintained 100% of the time.
As possible it makes sense to set-up your workstation within your Reach Zone. True/False
The Power Position:
Is a “ready” position for almost every sport.
Can be used when lifting a box.
Can be used when getting a drink at the water fountain.
All of the above.
It is possible to eliminate fatigue from our day-to-day activities. True/False
Ideas to control fatigue include:
Alternating job tasks throughout the day.
Taking appropriate recovery breaks
Maintaining adequate hydration.
Using stretching as “microbreaks”.
All of the above.
Notes: Please go back and review the information for any questions you missed.

## Slide 32: Work-Related Musculoskeletal Disorders
Absence of sound ergonomics workplace environment and work practices
  Lead to physical ailments termed Work-related Musculo Skeletal Disorders (WMSDs)
WMSDs - Defined
  Muscles, joints, nerves, tendons, ligaments, cartilage, or spinal discs
Notes: The absence of a sound ergonomics workplace environment and work practices can lead to a variety of physical ailments termed work-related musculoskeletal disorders (WMSDs).
Other terms include Cumulative Trauma Disorders (CTDs), or Repetitive Strain Injuries (RSIs).
Work-related musculoskeletal disorders involve the muscles, joints, nerves, tendons, ligaments, cartilage, or spinal discs. Mainly occurring in the back, neck, arms, and wrists they typically reflect a gradual onset of symptoms.

## Slide 33: Work-Related Musculoskeletal Disorders
Onset of WMSDs
  Gradual onset of symptoms, results from longer-term wear and tear on body
  Single episode like lifting a too heavy load in an awkward position
Notes: For instance, many WMSDs result from longer-term wear and tear on the body.
However, a single episode like lifting a too heavy load in an awkward position may result in trauma.
Whether gradual or sudden onset, the objective is to recognize the potential risk factors.
Experience tells us that utilizing the ergonomics assessment process will assist you in applying the ergonomics principles to make a positive difference for yourself.

## Slide 34: Causes of WMSDs
Factors include
  Awkward postures
  Overhead reaching
  Twisting body
Other recognized WMSD factors
  Highly repetitive activities - pipetting and screwing/unscrewing caps on lab samples
  Contact stress - resting wrists and forearms on edge of surface
  Contact stress - leaning forward with elbows on surface
Notes: What factors have the potential to result in WMSDs?
Factors include awkward postures, overhead reaching, and twisting the body.
Other recognized WMSD factors are highly repetitive activities like pipetting and screwing/unscrewing caps on lab samples and contact stress like resting the wrists and forearms on the edge of a surface or leaning forward with the elbows on the surface.

## Slide 35: Most Common WMSDs in Labs
WMSD | Cause | Lab Tasks
Rotator Cuff Tendinitis | Repetitive tasks with elbows above mid-torso height | Biosafety Cabinets
DeQuervains Tendinitis | Forceful grasping and turning | Volumetric handling
Trigger Finger | Repetitive use of tools with sharp handles or hard edges | Pipetting
Thoracic Outlet Syndrome | Arm elevation | High workstation
Notes: Specific to laboratory tasks here is a list of common WMSDs with potential causes.
For example, use of Biosafety Cabinets with repetitive tasks involving elbows positioned above the mid-chest height have the potential to result in shoulder Rotator Cuff Tendonitis.
Forceful hand grasping and turning associated with volumetric handling may be correlated with DeQuervains Tendinitis (tendonitis of a thumb tendon).
Manual pipetting involving repetitive use of tools with sharp handles or hard edges may be related to Trigger Finger (a condition in which a finger gets stuck in a bent position and then snaps straight).
A workstation that is too high resulting in arm elevation may be related to Thoracic Outlet Syndrome (a condition affecting the upper extremity nerves and blood vessels).

## Slide 36: Medical Intervention
Not everyone will develop WMSDs
  Important to understand WMSD basics
  Identify potential issues early on
  Enact preventive measures
Don’t allow small issues to develop into major ones!
  Report any significant medical issues to appropriate individuals in workplace
Notes: Of course, not everyone who performs laboratory tasks will develop WMSDs; however, it is important you understand the basics of WMSDs so you can identify any potential issues early on and most importantly enact preventive measures.
Don’t allow small issues to develop into major ones!
Report any significant medical issues to the appropriate individuals in your workplace.

## Slide 37: Questions on WMSDs
Work-related musculoskeletal disorders involve the muscles, joints, nerves, tendons, ligaments, cartilage, or spinal discs. True/False
WMSDs may result from:
Longer-term wear and tear on the body.
A single episode activity like lifting.
Both A. and B.
Recognized WMSD factors include:
Repetitive activities like pipetting and screwing/unscrewing caps on lab samples.
Contact stress like resting wrists and forearms on the edge of a surface or leaning forward with elbows on surface.
Awkward postures, overhead reaching, and twisting the body.
All of the above.
The best solution for WMSDs is to ignore them and hope they will go away. True/False
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 38: Questions on WMSDs
Work-related musculoskeletal disorders involve the muscles, joints, nerves, tendons, ligaments, cartilage, or spinal discs. True/False
WMSDs may result from:
Longer-term wear and tear on the body.
A single episode activity like lifting.
Both A. and B.
Recognized WMSD factors include:
Repetitive activities like pipetting and screwing/unscrewing caps on lab samples.
Contact stress like resting wrists and forearms on the edge of a surface or leaning forward with elbows on surface.
Awkward postures, overhead reaching, and twisting the body.
All of the above.
The best solution for WMSDs is to ignore them and hope they will go away. True/False
Notes: Please go back and review the information for any questions you missed.
.

## Slide 39: Warm-up and Stretching
Benefits
  Minimizes likelihood of injury
  Enhances performance
Specifically doing to warm up and stretch as part of job?
  If the answer is . . . nothing
  Increasing risk of suffering musculoskeletal disorder
  Limiting level of job performance
Notes: Anyone who plays a sport knows the importance of warming up and stretching for two primary reasons:
It minimizes the likelihood of injury and enhances performance.
Your job certainly involves physical activity. What are you doing specifically to warm up and stretch as part of your job?
If the answer is . . . nothing, you are increasing the risk of suffering a musculoskeletal disorder and limiting the level of your job performance.

## Slide 40: Warm-up and Stretching
Stretching not only primes body:
  Increases blood flow to working tissues providing more oxygen and nutrition
  Loosen joints to decrease stiffness
  Improve alertness levels through increased levels of oxygen in blood going to brain
Think of it, all of this just from stretching!
Notes: Stretching not only primes the body:
It also increases blood flow to the working tissues providing more oxygen and nutrition
It helps to loosen the joints to decrease stiffness and
It helps to improve alertness levels through increased levels of oxygen in the blood going to the brain.
Think of it, all of this just from stretching.

## Slide 41: Warm-up and Stretching Guidelines
Follow any specific medical restrictions
Warm-up by performing a few repetitive movements
  Making and opening a fist or performing shoulder rolls
Always stretch from neutral position
Use slow controlled movements
Push stretch only as far as is comfortable for you
You should feel a stretch not pain
Listen to your body - Stop stretch if experience any numbness or tingling
Don't hold breath during stretch – breathe in with stretch and out with relaxation
Notes: Guidelines for stretching include:
Follow any specific medical restrictions
Warm-up by performing a few repetitive movements such as making and opening a fist or shoulder rolls
Always stretch from the neutral position
Use slow controlled movements
Push the stretch only as far as is comfortable for you
You should feel a stretching not pain
Listen to your body - Stop the stretch if you experience any numbness or tingling
Don't hold your breath during the stretch – breathe in with the stretch and out with the relaxation

## Slide 42: Selected Stretches
Handout
Click on the icon to the right of the title to open the document.
Stretching Poster
Notes: Handout
In PowerPoint Normal View click on the icon to the right of the title to open the document.
See the Resources slide for other handouts and resources.

## Slide 43: Questions on Warm-up and Stretching
Warm-up and Stretching:
Increases blood flow to the working tissues providing more oxygen and nutrition.
Helps to loosen the joints to decrease stiffness.
Improves alertness levels.
All of the above.
The following guidelines should be followed with a stretching program:
Ignore any specific medical restrictions.
Always stretch from the neutral position.
Use fast jerky movements.
Push the stretch only as far as is comfortable for you.
Listen to your body - stop the stretch if you experience any numbness or tingling.
B. D. and E. above.
When you stretch you should hold your breath the entire duration of the stretch. True/False
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 44: Questions on Warm-up and Stretching
Stretching:
Increases blood flow to the working tissues providing more oxygen and nutrition.
Helps to loosen the joints to decrease stiffness.
Improves alertness levels.
All of the above.
The following guidelines should be followed with a stretching program:
Ignore any specific medical restrictions.
Always stretch from the neutral position.
Use fast jerky movements.
Push the stretch only as far as is comfortable for you.
Listen to your body - stop the stretch if you experience any numbness or tingling.
B. D. and E. above.
When you stretch you should hold your breath the entire duration of the stretch. True/False
Notes: Please go back and review the information for any questions you missed.

## Slide 45: Physical Fitness and Health and Wellness
Well-balanced Physical Fitness Program
  Job provide all components of well-rounded, well-balanced physical fitness program?
  More than likely the answer is NO.
Individuals with balanced personal physical fitness less likely to sustain injury
Strength, flexibility and aerobic endurance
Notes: When we talk about overall personal physical fitness does your job provide all the components of a well-rounded, well-balanced physical fitness program?
Does it provide all the strength, flexibility and heart and lung fitness you need?
More than likely the answer is NO.
Many studies have shown that individuals with balanced personal physical fitness are less likely to sustain an injury.
So, physical fitness is a combination of strength, flexibility and aerobic endurance. To better meet your job demands you can perform a variety of exercises at home or a fitness center.

## Slide 46: Very Important Point
If you have any health concerns about starting a physical fitness program you should always consult with your health care professional before starting.
Notes: HERE IS A VERY IMPORTANT POINT: If you have any health concerns about starting a physical fitness program you should always consult with your health care professional before starting.

## Slide 47: Personal Health and Wellness
Factors:
  Adequate diet and nutrition
  Body weight control
  Stress management
  Smoking cessation
  Blood pressure control
  Adequate rest from sleep and
  Fluid intake to avoid getting dehydrated
Factors under our control
  Personal physical fitness and health and wellness
Notes: In addition to physical fitness what about overall personal health and wellness?
It’s up to you: Your personal health and wellness, just like your personal physical fitness, is your personal business.
Here is a list of health and wellness factors to consider:
Adequate diet and nutrition
Body weight control
Stress management
Smoking cessation
Blood pressure control
Adequate rest from sleep and
Fluid intake to avoid getting dehydrated
These are all factors under our control that can help us be healthy and well.
No doubt . . . personal physical fitness and health and wellness are part of an overall strategy for a healthy and safe place to work.

## Slide 48: Questions on Physical Fitness and Health/Wellness
Physical Fitness and Health and Wellness include factors under our control that can help us be healthy and well. True/False
If you have any health concerns about starting a physical fitness program it is not advisable to consult with your health care professional before starting. True/False
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 49
Physical Fitness and Health and Wellness include factors under our control that can help us be healthy and well. True/False
If you have any health concerns about starting a physical fitness program it is not advisable to consult with your health care professional before starting. True/False
Questions on Physical Fitness and Health/Wellness
Notes: Please go back and review the information for any questions you missed.

## Slide 50: Ergonomics Workstation Assessment
Worksheet
We have included the USDA APHIS Laboratory Ergonomics Assessment Worksheet
Click on the icon to the right of the title to open the document.
Ergonomics Workstation Assessment Worksheet
Notes: Now that you have a handle on the ergonomics principles of Neutral Position, Reach Zone, Power Position and Fatigue Control let’s pull it all together into the ergonomics problem solving approach.
Whether it’s a task you’ve done many times or a brand-new one, take yourself through this step-by-step approach.
We have included the Ergonomics Workstation Assessment Worksheet for you to fill out to complete the assessment.

## Slide 51: Step One – Identify Task
First step is to identify workstation or task want to analyze
  Existing workstation or task
  One that is new
Notes: An obvious first step is to identify the workstation or task you want to analyze.
This could be an existing workstation or task or one that is new.

## Slide 52: Step Two – Apply Ergonomics Principles
Neutral Position and Support
  What is your body and limb position?
  Able to reasonably work in Neutral Positions (able to support body and limbs in neutral position)?
  If not, try to identify why not
Notes: What is your body and limb position? Are you able to reasonably work in Neutral Positions (think about the mid-range of joint position concept)?
Are you able to support your and body and limbs in the neutral position?
If not, try to identify why not.

## Slide 53: Step Two – Apply Ergonomics Principles
Neutral Position and Support
For example
  Is the worksurface too low?
  Is your chair or stool not properly adjusted?
  Does the tool or equipment not allow a neutral position?
Then think about how you can make it better
Notes: For example:
Is the worksurface too low?
Is your chair or stool not properly adjusted?
Does the tool or equipment not allow a neutral position?
Then think about how you can make it better.

## Slide 54: Step Two – Apply Ergonomics Principles
Reach Zone
  Where are you using your hands?
  Are you able to primarily use them in your Reach Zone?
  If not, try to identify preventing factor
For example:
  Is work too far away?
  Physical barrier that limits access?
Then think about how you can make it better
Notes: Where are you using your hands? Are you able to primarily use them in your Reach Zone?
If not, try to identify the preventing factor.
For example:
Is the work too far away?
Is there a physical barrier that limits access?
Then think about how you can make it better.

## Slide 55: Step Two – Apply Ergonomics Principles
Power Position
  Are you able to use Power Position to accomplish task?
  If not, try to identify what is the limiting factor
For example:
  Is material being handled too low or too high?
  Does equipment in use not allow power position?
Then think about how you can make it better
Notes: Are you able to use the Power Position to accomplish the task?
If not, try to identify why.
For example:
Is the material being handled too low or too high?
Does the equipment in use not allow a power position?
Then think about how you can make it better.

## Slide 56: Step Two – Apply Ergonomics Principles
Fatigue Control
  Able to Control Fatigue through-out work shift?
  If not, what are inhibiting factors
For example:
  Using wrong tool or incorrectly
  Not taking recovery breaks?
  Becoming dehydrated?
  Not using stretching as micro-breaks through-out shift?
  A combination of above?
What actions can you take to control fatigue?
Notes: Are you able to Control Fatigue through-out the work shift?
If not, what are the inhibiting factor or factors.
For example:
Using the wrong tool or using a tool incorrectly?
Not taking appropriate recovery breaks?
Becoming dehydrated?
Not using stretching as micro-breaks through-out the shift?
A combination of the above?
What actions can you take to control fatigue?

## Slide 57: Step Three – Recommend/Implement Improvements
List of potential improvements
  Workstation set-up
  Particular use of a tool or piece of equipment
  Change of workstation, tool or equipment
To get some practice in ergonomics problem solving let’s go through an example
Notes: As you were performing the assessment you also were generating a list of potential improvements.
They might consist of workstation set-up improvement, particular use of a tool or piece of equipment or a change of the workstation, tool or equipment.
To get some practice in ergonomics problem solving let’s go through an example.

## Slide 58: Practice
Choose a task you would like to analyze and go through the USDA APHIS Laboratory Ergonomics Assessment Worksheet

## Slide 59: Question on Ergonomics Workstation Assessment
The steps of the Ergonomics Workstation Assessment include:
Identify the task to be assessed.
Apply the ergonomics principles to the current method of the task.
Generate recommendations and implement them.
All of the above.
Notes: Take a moment and answer the question. The answer is found on the next slide.

## Slide 60: Question on Ergonomics Workstation Assessment
The steps of the Ergonomics Workstation Assessment include:
Identify the task to be assessed.
Apply the ergonomics principles to the current method of the task.
Generate recommendations and implement them.
All of the above.
Notes: Please go back and review the information if you missed the question.

## Slide 61: Laboratory Ergonomics: Tips and Techniques
Ergonomics principles
Warm-up and Stretching, Physical Fitness and Health and Wellness.
Step-by-step ergonomics problem solving approach
Laboratory Ergonomics Tips and Techniques
  “Fit the Job to the Person!”
  “Work Smarter, Not Harder!”
Notes: We’ve covered a lot of information . . . the ergonomics principles of Neutral Posture and Support, Reach Zone, Power Position and Fatigue Control as well as information about Warm-up and Stretching, Physical Fitness and Health and Wellness.
We went through a specific step-by-step ergonomics problem solving approach to apply the ergonomics principles.
Next, let’s look at specific Laboratory Ergonomics Tips and Techniques.
See if they can work for you and apply them across the board to, “Fit the Job to the Person!” and “Work Smarter, Not Harder!”

## Slide 62: Laboratory Workbenches, Stools and Footrests
Workbenches at a fixed height Workbench may be user-controlled height adjustable
Stools available
  Ensure surface decontamination
Footrests for foot support
Set up workbench, stool and footrest to follow ergonomics principles
  Neutral position
  Reach zone
  Power position
  Fatigue control
Notes: Workbenches are commonly used in the lab to support equipment and perform procedures.
In many cases, laboratory workbenches are at a fixed height (typically about 36”) and have been designed using general guidelines suggested by the National Institute of Occupational Safety and Health (NIOSH). In some cases, the workbench may be user-controlled height adjustable.
Generally, stools are available to allow for a seated body position when working at the workbench.
Footrests are also included to provide for foot support when seated on the stool.
Recalling the goal is to “Fit the Job to the Person”, consider how to set up the workbench, stool and footrest to follow the ergonomics principles of neutral position and support, reach zone, power position and fatigue control.

## Slide 63: Workbench/Elbow Height Relationship
Based on tasks you are performing
Precision work, need to precisely view hands
  Fixed height workbench
    Elbow height about 2 to 4 inches above workbench height
  Adjustable height workbench
    Workbench height so elbows are about 4 to 6” above resting elbow height (this is with arms at sides)
Notes: First, recognize the relationship between your body and extremity position and the workbench is based on what tasks you are performing.
For a fixed height workbench, for precision work where you need to precisely view your hands, the recommended relationship is with elbow height about 2 to 4 inches above the workbench height.
For an adjustable height workbench, for precision work, adjust the workbench height so the elbows are about 4 to 6” above resting elbow height (this is with the arms at the sides).

## Slide 64: Workbench/Elbow Height Relationship
Based on tasks you are performing
General light work
  Handling test tubes, pipetting, etc.
Heavy work
  Downward force exerted (pushing down on tool or other materials)
Notes: For general light work (handling test tubes, pipetting, etc.) have the relationship so the workbench is at or slightly below elbow height, about 1 to 2 inches below.
For heavy work where a downward force needs to be exerted (pushing down on a tool or other materials) establish the relationship so the workbench is about 4 to 6 inches below elbow height.

## Slide 65: Workbench/Stool/Footrest Adjustment Strategies
Once you understand task to be performed
Follow adjustment strategies based on whether workbench
Fixed height or height adjustable
Notes: Once you understand the task to be performed follow these adjustment strategies based on whether the workbench is fixed height or height adjustable.

## Slide 66: Workbench Fixed Height
Adjust Stool Height
  Use height adjustment feature Establish desired physical relationship between elbow height and workbench height
Other Stool Adjustments
  Seat tilt forward and backward
  Back support height and angle adjustable
  Armrests, height adjustable to provide for forearm support
Notes: With a fixed height workbench (typically about 36” from the floor), use the height adjustment feature of the stool to establish the desired physical relationship between elbow height and workbench height.
Two to 4 inches above elbow height for precision work, about elbow height or slightly lower for light work and 4 to 6 inches below elbow height for heavy work.
In other words, you use the workbench height as the reference point and adjust the stool and footrest to match.
Check out what other adjustments are on the stool. The seat may be able to tilt forward and backward. The back support may be height and angle adjustable. Armrests may be attached to the stool; if so determine if they are height adjustable to provide for forearm support.
Apply the Neutral Position and Support and Reach Zone ergonomics principles to improve your overall position and support when setting up the stool.

## Slide 67: Workbench Fixed Height
Most important guideline for stool use
  Get out of it on a regular basis!
  Limit sustained seated positions to 30 minutes or less
Leg/Foot Clearance
Foot Support
  Foot ring primarily there to help you get on and off seat of stool
    Adjust footrest height
    Footrest and foot ring should be about same height
Notes: Remember the most important guideline for stool use is . . . get out of it on a regular basis! Try to limit sustained seated positions to 30 minutes or less. This is part of the Fatigue Control principle.
You may find obstacles (drawers, supplies and other materials) underneath workbenches that limit leg and foot access.
They need to be removed or relocated.
While most stools do have a foot ring under the seat, it does not provide for comfortable, long-term foot support.
The foot ring is primarily there to help you get on and off the seat of the stool.
Use a height adjustable footrest to provide for foot and leg support. Adjust the footrest height so when your feet are supported on the footrest you have even body weight through your thighs and hips on the seat of the stool. The footrest and foot ring should be about the same height.

## Slide 68: Workbench Adjustable Height
Adjust Stool Height
  Stool may not go lower enough to get feet on floor
    Need footrest for adequate foot support
Adjust Workbench Height
Other Stool Adjustments
  Seat tilt forward and backward
  Back support height and angle adjustable
  Armrests, height adjustable to provide for forearm support
Notes: In some labs, the workbench may be height adjustable and now the floor becomes the reference point for workbench set-up. Follow this strategy.
Determine if you can adjust the stool height to get your feet directly on the floor. This eliminates the need for foot support on a footrest.
Now, in some cases the stool may not go lower enough to get your feet on the floor, and you will still need a footrest for adequate foot support.
Next, adjust the workbench height based on the task at hand to establish the desired physical relationship between elbow height and workbench height.
For precision work, adjust the workbench height so the elbows are about 2 to 4” above resting elbow height (this is with the arms at the sides), for light work about elbow height or slightly lower and for heavy work about 4 to 6 inches below elbow height.
Check out what other adjustments are on the stool. The seat may be able to tilt forward and backward. The back support may be height and angle adjustable. Armrests may be attached to the stool; if so determine if they are height adjustable to provide for forearm support.
Apply the Neutral Position and Support and Reach Zone ergonomics principles to improve your overall position and support when setting up the stool.
Remember the most important guideline for stool use is . . . get out of it on a regular basis! Try to limit sustained seated positions to 30 minutes or less. This is part of the Fatigue Control ergonomics principle.

## Slide 69: Workbench Adjustable Height
Leg/Foot Clearance
Foot Support
  Foot ring primarily to help get on and off seat
    Adjust footrest height
    Footrest and foot ring should be about same height
Notes: You may find obstacles (drawers, supplies and other materials) underneath workbenches that limit leg and foot access. They need to be removed or relocated to provide for the needed clearance.
Ideally, the best place for the feet is directly on the floor; however, even with height adjustable workbenches this may not be possible. In this case a footrest will be required to provide for adequate foot and lower extremity support.

## Slide 70: Standing at a Workbench
Standing makes sense:
  Spending only a short time (a few minutes)
  Move frequently between different locations at workbench
  Handle heavier items (more than 5 pounds)
  Need to exert significant downward force (more than 10 pounds of force)
Notes: Some tasks may involve standing at a workbench.
Typically standing makes sense if you are spending only a short time (a few minutes) in the standing position, move frequently between different locations at the workbench, handle heavier items (more than 5 pounds) at the workbench or when you need to exert significant downward force (more than 10 pounds of force) at the workbench.

## Slide 71: Workbench Height - Standing
Apply same elbow and workbench height relationships for standing as for seated
  Precision work: 2 to 4” above elbow height
  General light work: about elbow height or slightly lower
  Heavy work: 4 to 6 inches below elbow height
Notes: As possible, try to apply the same elbow and workbench height relationships for standing as for seated workbenches: 2 to 4” above elbow height for precision work, about elbow height or slightly lower for light work and 4 to 6 inches below elbow height for heavy work.

## Slide 72: Workbench Height - Standing
Too low fixed height workbench - build up workbench height
  Platform on workbench top to position tools, equipment or materials
  Entire workbench itself raised on a permanent basis.
Notes: For a fixed height workbench that is too low for the needed task, it may be possible to build up the workbench height by placing a platform on the workbench top to position the tools, equipment or materials at the desired height.
In some instances, the entire workbench itself can be raised on a permanent basis.
Of course, before doing this consult with others in the lab to make sure it won’t raise unintended consequences for others using the workbench.
And of course, if it is raised up ensure it is stable at the higher height.

## Slide 73: Footrests - Standing
Promote neutral position and increased comfort when standing
  Footrest to put one foot up on footrest and then alternate with other foot
  Utilize footwear with significant cushioning and support
    Good walking shoes are good standing shoes
  Shift weight forward to balls of feet and backwards to heels
  Perform “heel lifts” frequently
Notes: A great way to promote neutral position and increased comfort when standing is to provide a footrest that will allow you to put one foot up on the rest and then alternate with the other foot.
This promotes varied standing postures and intermittently redistributes weight-bearing stresses.
Utilize footwear that has significant cushioning and support.
If they are good walking shoes, they will also be good standing shoes.
Shift weight forward to the balls of the feet and backwards to the heels when standing on both feet or alternately when standing with one foot in front of the other.
Perform “heel lifts” frequently. This will improve lower extremity circulation.

## Slide 74: Anti-fatigue Mats - Standing
Anti-fatigue standing mats cushion feet and joints of ankles, knees, hips and back
  Large enough to allow for at least shoulder width foot placement
  Beveled mat edges to eliminate any trip hazard
  Adequate cleaning of mat and underlying floor
Notes: At workbenches where sustained standing is performed, consider adding anti-fatigue standing mats to cushion the feet and weight bearing joints of the ankles, knees, hips and back.
Mats should be large enough to allow for at least shoulder width foot placement.
Mat edges should be beveled to eliminate any trip hazard.
Adequate cleaning of the mat and underlying floor on a regular basis is necessary to provide for appropriate hygiene.

## Slide 75: Anti-fatigue Mats - Standing
Stools and mats
  Most stools will not roll easily on mats
    Mat is pushed out of the way and not used as it should be
    More sustained standing than is recommended occurs
Notes: A last comment about mats; mats and stools don’t play well together in the same neighborhood.
Most stools will not roll easily on the mats and the result is either the mat is pushed out the way and not used as it should be or more sustained standing than is recommended occurs because of the difficulty in rolling the stool into place.
In this case, eliminating the mat and ensuring footwear with significant cushioning and support is a viable option.
Another option is to secure a mat that can easily be moved and replaced by using your foot, rather than bending over.

## Slide 76: Questions on Workbenches and Stools
When performing precision tasks at a fixed height workbench of 36” your elbows should be:
Two to 4 inches above the workbench height.
At or slightly below (1 to 2 inches) below elbow height.
Four to 6 inches below elbow height
It doesn’t make any difference.
For a fixed height workbench you may be able to adjust the stool height to achieve the desired position. True/False
The foot ring on the stool is:
The best place to position your feet for the entire time you are on the stool.
Used primarily to assist in getting onto and off the stool.
None of the above.
When standing at a workbench:
Utilize footwear that has significant cushioning and support.
As possible match the workbench height to your elbow position for the task at hand.
Use a standing mat for foot comfort.
Use a footrest that will allow you to put one foot up on the rest and then alternate with the other foot.
All of the above.
It is worth the time it takes to adjust the stool to fit your particular workstation set-up needs. True/False
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 77: Questions on Workbenches and Stools
When performing precision tasks at a fixed height workbench of 36” your elbows should be:
Two to 4 inches above the workbench height.
At or slightly below (1 to 2 inches) below elbow height.
Four to 6 inches below elbow height
It doesn’t make any difference.
For a fixed height workbench you may be able to adjust the stool height to achieve the desired position. True/False
The foot ring on the stool is:
The best place to position your feet for the entire time you are on the stool.
Used primarily to assist in getting onto and off the stool.
None of the above.
When standing at a workbench:
Utilize footwear that has significant cushioning and support.
As possible match the workbench height to your elbow position for the task at hand.
Use a standing mat for foot comfort.
Use a footrest that will allow you to put one foot up on the rest and then alternate with the other foot.
All of the above.
It is worth the time it takes to adjust the stool to fit your particular workstation set-up needs. True/False
Notes: Please go back and review the information for any questions you missed.

## Slide 78: Pipetting
Pipetting – Common Task
  Pipetting is very common task in lab
  Repetitive nature, can be a source of hand and shoulder problems
Notes: Pipetting is a very common task in the lab. Because of the repetitive nature of pipetting, it can be a source of hand and shoulder problems.

## Slide 79: Pipettes – Workstation Set-up/Work Practices
Approximately same equipment, tray and supply heights
Within easy reach in logical work order
Prevent twisting and bending of wrist, neck and arms, elevation of shoulders and overreaching
Notes: To set-up the pipetting workstation, equipment, tray and supply heights should all be approximately the same and these items should be within easy reach in a logical work order.
Prevent twisting and bending of the wrist, neck and arms, elevation of the shoulders, and overreaching, by adjusting the height and position of various tools and equipment.

## Slide 80: Pipettes – Workstation Set-up/Work Practices
Adjusting height and position of various tools and equipment
  Sample holders (placed on a tilt)
  Solution container positioned within reach
  Waste receptacles – kept at low height (no higher than top of tube being filled)
  Work with arms close to the body
  Avoid arm elevation without support for lengthy periods
  Keep samples and instruments within easy reach
Notes: This can include:
Sample holders (placed on a tilt)
Solution containers positioned within reach
Waste receptacles – kept at a low height (no higher than top of tube being filled)
Work with the arms close to the body
Avoid arm elevation without support for lengthy periods
Keep samples and instruments within easy reach

## Slide 81: Pipette Design - Choices
Hand size
  Correlating hand size to pipette size
  Different sizes available
  Correct size pipette will allow hand to comfortably grasp/manipulate pipette
Weight
  Light weight as possible
Force
  Little force required as possible
Notes: Considerations for pipette design choices are highly individual:
Correlating hand size to pipette size is most important. Different sizes are available. The correct size pipette will allow your hand to comfortably grasp and manipulate the pipette.
As possible use a lightweight pipette; this requires less force to hold.
As possible use a pipette that requires as little force as possible to control.

## Slide 82: Pipette Design - Choices
Location of Controls
  Multi-finger pipette controls help distribute force among several fingers rather than continuously using same finger
  Button on top requires thumb to be repeatedly extended out of a relaxed, neutral position.
    Try to avoid and if not possible to avoid entirely, remember to limit sustained use as possible
Notes: Multi-finger pipette controls help distribute the force among several fingers rather than continuously using the same finger.
Some pipettes have a button on the top which may require the thumb to be repeatedly extended out of a relaxed, neutral position.
Try to avoid this type and if not possible to avoid entirely, remember to limit sustained use as possible.

## Slide 83: Pipetting - Guidelines
Short pipettes preferable to decrease hand and arm elevation
Pipettes where thumb dispenses and index finger aspirates
Pipette usage alternated between right and left hand
Clean pipettes regularly to reduce "sticking" and improve quality of work
Use thin-walled pipette tips that are easy to eject
Notes: In general, here are some overall guidelines for pipette use:
Short pipettes are preferable to decrease hand and arm elevation
Pipettes where the thumb dispenses, and the index finger aspirates are best
Pipette usage should be alternated between the right and left hand
Clean pipettes regularly to; reduce "sticking" and improve quality of work
Use thin-walled pipette tips that are easy to eject

## Slide 84: Manual vs Power Pipettes
Power pipettes rather than manual pipettes help to reduce hand stress and exertion
  Electronic operated or a latch-mode pipette to replace manual plunger-operated pipettes
  Electronic pipette with mixing functions for tasks such as mixing or aliquotting
  Multichannel pipette for large aliquotting tasks
Notes: Power pipettes rather than manual pipettes can help to reduce hand stress and exertion.
If possible, use an electronic operated or a latch-mode pipette to replace manual plunger-operated pipettes, use an electronic pipette with mixing functions for tasks such as mixing or aliquotting and use a multichannel pipette for large aliquotting tasks.

## Slide 85: Microbreaks and Task Rotation
Focus on Fatigue Control throughout day
  Take micro-breaks of 2 minutes for every 20 minutes of pipetting
    Alternate between right and left hands
    Alternate among different laboratory tasks
    Alternate among different people
  Perform hand stretches frequently
  Rotate pipetting activities
    Between right and left hands
    Among different laboratory tasks
    Different people
Notes: Focus on Fatigue Control throughout the day.
Take micro-breaks of 2 minutes for every 20 minutes of pipetting.
Perform hand stretches frequently.
Rotate pipetting activities between right and left hands, among different laboratory tasks and different people to reduce the overall exposure to the task.

## Slide 86: Questions on Pipetting
When pipetting you can prevent twisting and bending of the wrist, neck and arms by:
Positioning solution container outside your reach.
Keeping waste receptacles at a low height; no higher than top of tube being filled.
Working with your arms away from your body.
Elevating your arms without support for lengthy periods.
A good strategy to control fatigue when pipetting is to work as fast and as for long as you can to get the job done quickly. True/False
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 87: Questions on Pipetting
When pipetting you can prevent twisting and bending of the wrist, neck and arms by:
Positioning solution container outside your reach.
Keeping waste receptacles at a low height; no higher than top of tube being filled.
Working with your arms away from your body.
Elevating your arms without support for lengthy periods.
A good strategy to control fatigue when pipetting is to work as fast and as for long as you can to get the job done quickly. True/False
Notes: Please go back and review the information for any questions you missed.

## Slide 88: Microscopy
Microscopy – Common Task
  Operating microscope is very common task Potential exists for strain
    Neck
    Shoulders
    Eyes
    Lower back
    Arms
    Wrists
Notes: Operating a microscope is a very common task in the lab. Potential exists for strain of the neck, shoulders, eyes, lower back, arms and wrists.

## Slide 89: Microscope Set-up Before and After Example
Working at microscope that is not at correct height and angle results in
  A hunched-forward position, uncomfortable position of neck, shoulders, arms, back and hips.
  Contact stress on forearms from work surface edge.
Notes: Look at the before and after microscope set-up example. Very apparent, isn’t it, which one looks comfortable, safe and productive.
Working at a microscope that is not at the correct height and angle results in:
A hunched-forward position, uncomfortable position of the neck, shoulders, arms, back and hips.
Contact stress on the forearms from the work surface edge.

## Slide 90: Microscopy – Workstation Set-up
Multi-user
  Variety of individuals in lab
  Critically important each user take time to set-up microscopy workstation for their unique needs
Notes: Most microscopes will be used by a variety of individuals in the lab.
As a result, it is critically important that each user take the time to set-up the workstation for their unique needs.
Applying the ergonomics principles of Neutral Position and Support, Reach Zone, Power Position and Fatigue Control to the set-up process will enhance the comfort, safety and productivity of microscope use.

## Slide 91: Microscope Step-by-Step Set-up Protocol
Understand Adjustment Options
  Analyze current set-up to make sure you fully understand what adjustment options exist
    Height and angle of microscope itself
    Microscope eyepiece height and angle
    Stool or chair seat height, back support and armrests
    Worksurface
Notes: Follow this step-by-step set-up protocol for microscope use.
First analyze the current set-up to make sure you fully understand what adjustment options exist. For example, can you adjust the height and angle of the microscope itself, the microscope eyepiece height and angle, the stool or chair seat height, back support and armrests and/or the worksurface?

## Slide 92: Neutral Position/Support, Reach Zone
  Adequate room for legs so you can sit directly under microscope
  Adjust stool or chair
  If needed, provide a footrest
  Position microscope towards edge of work surface
  Position your head upright and your line of sight approximately 20 to 30º below straight-ahead vision
Notes: Once you have a handle on what adjustment options exist:
Position the scope so you have adequate room for your legs so you can sit directly under the microscope
Adjust the stool or chair to enhance neutral body position and support
Provide a footrest if needed to ensure adequate foot and leg support
Position the microscope towards the edge of the work surface to allow for neutral head and neck position
Position your head upright and your line of sight approximately 20 to 30º below straight-ahead vision

## Slide 93: Neutral Position/Support, Reach Zone
  Adjust microscope to match neutral head and neck position
  Adjust eyepieces and angle of view
  Use chair armrests to support forearms with elbows at sides
  Apply padding (foam rolls or padded edge protectors) to edge of work surface
  Padded angled microscope forearm supports to relieve fatigue and strain
Notes: Adjust the height of microscope to match your neutral head and neck position; the microscope maybe on a vertical support bar or an adjustable height platform
Adjust the eyepieces and angle of view to allow for a balanced position of your head on your shoulders
If they can be adjusted, use chair armrests to support your forearms with elbows at your sides.
If your forearms are in contact with edge of the worksurface, apply padding (foam rolls or padded edge protectors) to the edge of the work surface
If chair armrests interfere with your arms, remove them from chairs and consider use of padded angled microscope forearm supports to relieve fatigue and strain

## Slide 94: Fatigue Control
Employ fatigue control measures
Take 2-minute micro-breaks every 20 minutes of microscope use
Stretch to promote circulation and reduce joint stiffness
Rotate between variety of laboratory tasks
Mix it up throughout day
Notes: Employ your fatigue control measures.
Take a 2-minute micro-break every 20 minutes of microscope use.
Stretches are beneficial to promote circulation and reduce joint stiffness.
Rotate between a variety of laboratory tasks.
Mix it up throughout the day.

## Slide 95: Microscopy – Other Tips
Tilt storage bins toward you
Enlarge handle diameter of small hand tools by placing cylindrical foam around them
Make simple tool modifications
Notes: Here are some other tips.
Tilt storage bins toward you to reduce awkward postures while reaching for supplies.
Enlarge the handle diameter of small hand tools by placing cylindrical foam around them.
Make simple tool modifications if you are not able to keep your wrists straight.

## Slide 96: Microscopy - Control Eye Strain
Scope is clean
Lighting is adequate
Microscope lamp and optical pathway correctly aligned
Looking at distance point (more than 10 to 15 feet away) allows eyes to relax
Notes: Microscope use is obviously very visually intensive. Work to control eye strain.
Make sure the scope is clean, lighting is adequate, and the microscope lamp and optical pathways are correctly aligned.
Give your eyes a break by periodically looking at a distance point (more than 10 to 15 feet away).

## Slide 97: Microscopy - Control Eye Strain
Control excessive glare and reflections from overhead lighting
Adjust internal microscope light
Temperature and humidity conditions affect eyes
  Ambient temperature range of 66 to 73º Fahrenheit is suggested
  Eye drops can be beneficial for some, but should not be applied in the lab environment
Notes: Check the lab environment for excessive glare and reflections from overhead lighting and adjust the internal microscope light to compensate.
Temperature, humidity, air currents, ventilation, excessive noise, and ambient lighting levels affect operator comfort and fatigue.
Temperature range of 66 to 73º Fahrenheit is suggested.
Low humidity conditions lead to drying of the eyes; eye drops can be beneficial for some but should not be applied in the lab environment.

## Slide 98: Video Display Microscopy
Becoming more viable with technological improvements
When possible, use a video display terminal to view the sample
Monitor placement
  Top of screen is about at eye level
  Viewing distance about 24 to 28 inches
  Positioned directly in front
Notes: Video display microscopy is becoming more viable with technological improvements.
When possible, use a video display terminal to view the sample.
Place the display monitor so the top of the screen is about at eye level, viewing distance is about 24 to 28 inches and the display positioned directly in front of you so you can look straight ahead, not turning your head to the side
Overall, take the time to set-up the microscope workstation for your unique needs. It is time well spent!

## Slide 99: Questions on Microscopy
Because most microscopes will be used by a variety of individuals, it is critically important that each user take the time to set-up the microscopy workstation for their unique needs. True/False
Setting up the microscope workstation includes the following steps:
Position the scope for adequate room for your legs.
Adjust the stool or chair to enhance neutral body position and support.
Provide a footrest if needed to ensure adequate foot and leg support.
Adjust the height of microscope to match your neutral head and neck position.
Adjust the eyepieces and angle of view to allow for a balanced position of your head on your shoulders
None of the above.
All of the above.
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 100: Questions on Microscopy
Because most microscopes will be used by a variety of individuals, it is critically important that each user take the time to set-up the microscopy workstation for their unique needs. True/False
Setting up the microscope workstation includes the following steps:
Position the scope for adequate room for your legs.
Adjust the stool or chair to enhance neutral body position and support.
Provide a footrest if needed to ensure adequate foot and leg support.
Adjust the height of microscope to match your neutral head and neck position.
Adjust the eyepieces and angle of view to allow for a balanced position of your head on your shoulders
None of the above.
All of the above.
Notes: Please go back and review the information for any questions you missed.

## Slide 101: Lab Hoods or Biosafety Cabinets
An integral part of lab
Similar hazards as for microscope work
  Hunched postures
  Forward reaches
Ergonomics principles enhance use
Notes: An integral part of the lab is the use of lab hoods or biosafety cabinets (BSCs).
Similar hazards as for microscope work are seen with hunched postures and forward reaches.
Ergonomics principles of Neutral Position and Support, Reach Zone, Power Position and Fatigue Control go a long way to enhance BSC use.

## Slide 102: Lab Hoods or BSCs – Work Practices and Tips
Work practices and tips:
  If standing at lab hood or BSC, use anti-fatigue matting and wear supportive shoes
  Position materials as close as possible to avoid extended reaching
  Use a turntable to store equipment close at hand, this prevents reaching and twisting
Notes: Follow these work practices and tips.
If standing at the BSC, use anti-fatigue matting and wear supportive shoes.
Position materials as close as possible to avoid extended reaching.
Use a turntable to store equipment close at hand. This prevents reaching and twisting.

## Slide 103: Lab Hoods or BSCs – Work Practices and Tips
Reduce contact stress to forearms & wrists:
  Apply closed-cell foam padding to the front edge of the lab hood or BSC
  Make sure the padding can be decontaminated
Armrests
  Support arms at correct height and angle
  Do not restrict air flow
  Bubble wrap that is disposable and inexpensive
Notes: To reduce contact stress to forearms and wrists:
Apply closed-cell foam padding to the front edge of the BSC.
Make sure the padding can be decontaminated.
Attach external armrests to the cabinet to support the arms at the correct height and angle.
Make sure they do not restrict air flow. Where decontamination is a problem, consider the use of bubble wrap that is disposable and inexpensive.

## Slide 104: Lab Hoods or BSCs – Work Practices and Tips
Seated at BSC
  Fully adjustable chair or stool
  Provides adequate back support, adjustable seat angle, and height adjustability
  Adequate leg and thigh clearance under cabinets
  Raise cabinet couple of inches if necessary and possible
  Use footrest to provide stability in leaning forward from hips
Chair/stool options
  Sit-stand stools (Salli or Bambach)
Notes: If seated at the BSC, use a fully adjustable chair or stool that provides adequate back support, adjustable seat angle, and height adjustability.
Ensure adequate leg and thigh clearance under the cabinet.
Raise the cabinet a couple of inches if necessary and possible
Use a footrest, not the chair ring, to provide stability in leaning forward from the hips.
This reduces pressure on the back of the legs.
Consider the use of a seat height and angle adjustable sit-stand stool such as the Salli or Bambach Stool.

## Slide 105: Newer BSCs
Height adjustable tables with downdraft or backdraft
  Eliminate bent, forward posture of traditional BSCs
Other improvements
  Perforated front grill reduced by 1-2 inches allows work platform to be closer to worker
  Non-glare glass on sash window
  Adjustable plexiglass barriers
  Platform with wells for placement of tall containers to reduce reaching
Notes: Newer BSCs that have height adjustable tables with downdraft or backdraft rather than the traditional updraft exhausting are being seen more and more. They eliminate the bent, forward posture of traditional BSCs.
Other improvements are a perforated front grill reduced by 1-2 inches that allows the work platform to be closer to the worker, non-glare glass on the sash window, adjustable plexiglass barriers and a platform with wells for placement of tall containers to reduce reaching.
Use ergonomics to your advantage when using BSCs.

## Slide 106: Question on Lab Hoods or Biosafety Cabinets
Ergonomics principles of Neutral Position and Support, Reach Zone, Power Position and Fatigue Control go a long way to enhance BSC use. True/False
Notes: Take a moment and answer the question. The answer is found on the next slide.

## Slide 107: Question on Lab Hoods or Biosafety Cabinets
Ergonomics principles of Neutral Position and Support, Reach Zone, Power Position and Fatigue Control go a long way to enhance BSC use. True/False
Notes: Please go back and review the information if you missed the question.

## Slide 108: Test Tube Handling Tips
Body posture
  Adjust chair properly to provide adequate back support
  Remove chair arms if interfere with ability to get close to work
Arrange tubes
Open/close test tubes
  Use both hands to open and close
    Rotate cap in one direction with one hand while rotating tube in opposite direction with other hand
Notes: Handling test tubes is a very common task in the lab. Here are some ideas to enhance test tube handling.
Whole body posture comes into play. Adjust the chair properly before you start work so it provides adequate back support.
Remove the chair arms if they interfere with the ability to get close to your work.
Arrange tubes to minimize reaching and twisting by placing them as close as possible to you. Use a container to raise test tube racks when necessary. When possible use a vortexer mixer rack instead of holding tubes by hand.
Use both hands to open and close test tubes to lessen the stress on one hand or the other.
Rotate the cap in one direction with one hand while rotating the tube in the opposite direction with the other hand.

## Slide 109: Test Tube Handling Tips
Cap Removers
  Use cap removers to minimize pinch grip and stress on fingers
  Example is Gilson's Jimmy microtube opener
Automatic/powered capping/decapping equipment
  If screwing many similar microtubes, automatic/powered capping and de-capping equipment may be appropriate
Notes: Use cap removers to minimize pinch grip and stress on the fingers. An example is the Gilson's Jimmy microtube opener.
If screwing many similar microtubes, automatic or powered capping and de-capping tools and equipment may be appropriate.
See: https://nbsscientific.com/xqinstruments/#:~:text=XQ%20Instruments%20designs%20single%2Dtube,portable%2C%20and%20cost%2Defficient.

## Slide 110: Micro-Manipulation & Fine Motor Skills
Considerations
  Use plastic vials with fewer threads to reduce twisting motions during capping and uncapping lids
  Tilt storage bins toward you to reduce wrist flexion while reaching for supplies
  For forceps manipulation, use small pieces of foam, like type used on pencils and pens
  Practice using forceps between index and middle fingers instead of using thumb and index finger
Notes: Here are some miscellaneous tips for micro-manipulation of materials and tools that involves fine motor skills.
Use plastic vials with fewer threads to reduce twisting motions during capping and uncapping lids.
Tilt storage bins toward you to reduce wrist flexion while reaching for supplies.
For forceps manipulation, use small pieces of foam, like the type used on pencils and pens to prevent soreness on the fingertips.
Practice using forceps between the index and middle fingers instead of using the thumb and the index finger.

## Slide 111: Questions on Test Tube Handling
Arrange test tubes to minimize reaching and twisting by:
Placing them as far from you as possible to you.
Use container to raise test tube racks.
Use a vortexer mixer rack instead of holding tubes by hand.
Always use only one hand to open and close test tubes.
B and C above.
You can use cap removers to minimize pinch grip and stress on the fingers. True/False
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 112: Questions on Test Tube Handling
Arrange test tubes to minimize reaching and twisting by:
Placing them as far from you as possible to you.
Use container to raise test tube racks.
Use a vortexer mixer rack instead of holding tubes by hand.
Always use only one hand to open and close test tubes.
B and C above.
You can use cap removers to minimize pinch grip and stress on the fingers. True/False
Notes: Please go back and review the information for any questions you missed.

## Slide 113: Material and Equipment Handling
What is the very first guideline for safe material handling?
What is the safest lift you can do?
It’s the one you don’t do!
As appropriate, make sure you use equipment available to assist with or accomplish lift
Notes: Next let’s get into the specifics of using ergonomics principles for material and equipment handling. Lifting, pushing, pulling, carrying.
First though, what is the very first guideline for safe material handling?
Think of it this way.
What is the safest lift you can do? It’s the one you don’t do!
As appropriate, make sure you use the equipment available to assist with or accomplish the lift.

## Slide 114: Up-front Planning
Front planning minimizes stress and strain
  Allows you to get assistance if you need it
Understand your personal physical performance limit
  If you exceed your limit, significantly increase risk of injury
  Literally takes only a quarter of a second for a life-changing injury to take place
If you need help. . . get it!
Notes: When you do any type of material handling, up front planning goes a long way to minimize stress and strain and allows you to get assistance if you need it.
Understand what your personal physical performance limit truly is.
If you exceed your limit, you significantly increase your risk of injury. It can literally take only a quarter of a second for a life-changing injury to take place.
If you need help. . . get it!

## Slide 115: Power Lift Technique
Task within your personal performance limit
What is best technique?
  Professional weightlifters
  Power Lift makes use of Power Position
Up-front planning
  Need to use mechanical equipment or get someone to help you
  You have thought through where material is going to end up.
  You have anticipated any surprises
Notes: So, at this point you have determined the manual material handling task is within your personal performance limit and you are going to handle it.
What is the best technique to use?
Let’s turn to the technique commonly used by professional weightlifters.
They call it the Power Lift. It makes use of the ergonomics principle of the Power Position.
Remember you have done your up-front planning to decide if you need to use mechanical equipment or get someone to help you.
You have thought through where the material you are gong to handle is going to end up.
You have anticipated any surprises.

## Slide 116: Power Lift - Step-By-Step Details
Approach object with feet slightly wider than shoulder width
Good footing
Straddle object
Bend hips and knees somewhat, reach hands to object
Grip object, might be at a diagonal
Build “bridge” with elbow on knee to unload back
Notes: All right, first step . . . approach the object with your feet slightly wider than shoulder width.
Make sure you have good footing.
Straddle the object as much as possible almost making it a part of you.
Now bend your hips and knees somewhat and reach your hands to the object.
Figure out the best way to grip the object. This might be at a diagonal.
You can also build a bridge with your elbow on your knee to unload your back as you get your grip.

## Slide 117: Power Lift - Step-By-Step Details
Goal is to keep object as close as possible to you
Tighten up stomach muscles
At the moment of exertion . . . LOOK UP!
Why LOOK UP
  Automatically put you into Power Position
  Use large muscles of legs and thighs - not back to accomplish lift
  Back muscles work with stomach muscles to stabilize your spine
Notes: Your goal is to keep the object as close as possible to you.
Tighten up your stomach muscles.
You are now ready to lift!
One last critical step. . . at the moment of the exertion . . . LOOK UP.
Look up as you lift.
Looking up will automatically put you into the Power Position and you will use the large muscles of your legs and thighs - not your back to accomplish the lift.
Your back muscles will work with your stomach muscles to stabilize your spine in the neutral position.

## Slide 118: Practice Power Lift
Practice Power Lift technique to get comfortable with it
  May seem a bit strange at first
  Make it a habit and you will be amazed at the difference it makes
Feel stronger and more powerful using technique
That must be why it’s called the, “Power Lift”!
Notes: Practice the Power Lift technique to get comfortable with it. It may seem a bit strange at first. Make it a habit and you will be amazed at the difference it makes.
Many people who use the power lift say they feel stronger and more powerful using the technique.
That must be why it’s called the, “Power Lift”!

## Slide 119: Golfer’s Lift
Lighter weight item that you can handle with one hand
  Lift one leg back as you bend over at hip to reach to the item
  Counterbalances trunk
Practice using Golfer’s Lift
Notes: If you have a lighter weight item that you can handle with one hand use the Golfer’s Lift.
Lifting one leg back as you bend over at the hip to reach to the item counterbalances the trunk and works well.
Practice using the Golfer’s Lift as it makes sense for you.

## Slide 120: Two Stage Lift
Item to higher level
  Use power position to bend hips/ knees to start at higher position
  As you stand upright item is already at height you need it to be
  Makes good use of leg strength and not just arm strength
  Legs are stronger than arms!
Item at a distance
  Slide item to edge as first stage of lift
  Once its closer, use power lift technique to lift
Notes: A very effective technique is to break the lift into stages. For example, let’s say you have an item on a cart at about waist level that you need to get onto a higher level. You could try to muscle it up with your arms and shoulders . . . but that can put stress into the back.
With the two-stage lift, you actually use the power position.
You bend your hips and knees to start the item at a higher position, for example at chest or shoulder level.
Then as you stand upright the item is already at the height you need it to be.
You make good use of leg strength and not just arm strength. Legs are stronger than arms!
Or let’s say you are reaching away from you to pick up an item.
Maybe a box on a workbench.
Slide the box to the edge as the first stage of the lift and then once its closer, use the power lift technique.

## Slide 121: Bottom Line
Bottom line - use power position techniques to your advantage
Always use lift assistive devices that may be appropriate
  Better to have a device do the lift than the human.
Keep in mind your knowledge of your personal limit and always get assistance if you need it!
Notes: Bottom line - use the power position techniques to your advantage. But with any situation, always please use lift assistive devices that may be appropriate (hydraulic or pneumatic lift, etc.). Better to have a device do the lift than the human.
Keep in the front of your mind your knowledge of your personal limit and always get assistance if you need it.

## Slide 122: Questions on Material Handling
If possible, it makes sense to use lifting equipment to handle materials rather than do it manually. True/False
The Power Lift Technique includes this very important step:
Always look down when you lift.
Always look up when you lift
Make sure your feet are very close together when you lift.
Always use the Power Lift by yourself; do not ask for assistance.
Other techniques to handle materials include:
Golfer’s Lift
Two Stage lift
A and B
Notes: Take a moment and answer the questions. The answers are found on the next slide.

## Slide 123: Questions on Material Handling
If possible, it makes sense to use lifting equipment to handle materials rather than do it manually. True/False
The Power Lift Technique includes this very important step:
Always look down when you lift.
Always look up when you lift
Make sure your feet are very close together when you lift.
Always use the Power Lift by yourself; do not ask for assistance.
Other techniques to handle materials include:
Golfer’s Lift
Two Stage lift
A and B
Notes: Please go back and review the information for any questions you missed.

## Slide 124: Available Services
Individual Ergonomics Evaluations and/or Training Services
  For employees wishing to request an ergonomics evaluation or training services follow instructions listed in APHIS Ergonomics website
  https://www.aphis.usda.gov/aphis/ourfocus/business-services/emergency_management/ergonomics_program/
Notes: For employees wishing to request an ergonomics evaluation or training services follow the instructions listed in the APHIS Ergonomics website: https://www.aphis.usda.gov/aphis/ourfocus/business-services/emergency_management/ergonomics_program/

## Slide 125: Successful Ergonomics
Defined Work-related Musculoskeletal Disorders and common causes
Defined ergonomics
  “Fit the Job to the Person”
  “Work Smarter, Not Harder”
Outlined ergonomics principles
Lab Ergonomics Assessment Process
Notes: We’ve covered a lot of ground in the USDA APHIS Laboratory Ergonomics Training session.
We defined Work-related Musculoskeletal Disorders and common causes.
We defined ergonomics as, “Fit the Job to the Person” and “Work Smarter, Not Harder”, we outlined a set of ergonomics principles and we went through how to use the Lab Ergonomics Assessment Process.

## Slide 126: Successful Ergonomics
Personal physical fitness and health and wellness
Learned a series of stretches
Specific ergonomics tips and techniques:
  Pipetting
  Microscopy
  Biological safety cabinets
  Test tube handling
  Set-up of laboratory workstations
Notes: We outlined the benefits of personal physical fitness and health and wellness and you learned a series of stretches.
We detailed specific ergonomics tips and techniques for common laboratory tasks: pipetting, microscopy, use of biological safety cabinets, test tube handling and the set-up of laboratory workstations.

## Slide 127: Successful Ergonomics
All in all, we hope this information helps you be more comfortable, safe and productive in the lab!
Thanks for your time and attention!
Notes: All in all, we hope this information helps you be more comfortable, safe and productive in the lab.
Thanks for your time and attention!

## Slide 128: Resources
Mayo Clinic- video discusses creative solutions to control risk factors https://youtu.be/hB_k8_W1KjA2
Mayo Clinic - video discusses a lift assist device that can be used in a lab https://youtu.be/llQ8Pa3IwmM
Mayo Clinic - video addresses a screw cap tube device that can help with tube capping https://youtu.be/o2cy6p8uURg
Pipetting safety from UCLA https://youtu.be/bqAsXMSs27s
Electronic pipetting, https://youtu.be/vBMhtiypVuc
OSHA Fact Sheet: Laboratory Safety Ergonomics,
https://www.osha.gov/Publications/laboratory/OSHAfactsheet-laboratory-safety-ergonomics.html
UCLA Tips For Lab Workers, https://www.ergonomics.ucla.edu/laboratory-ergonomics/tips-for-lab-workers
OSHA Lab Fact Sheet – Prevention of Musculoskeletal Disorders, https://www.osha.gov/Publications/laboratory/OSHAfactsheet-laboratory-safety-ergonomics.pdf
Lab Manager – Laboratory Ergonomics, https://www.labmanager.com/lab-health-and-safety/laboratory-ergonomics-20312
Laboratory Checklist, http://www.wsha.org/wp-content/uploads/Worker-Safety_Lab-Ergo-Checklist-HumanFit.pdf