## Slide 1
Introduction to Ergonomics
MENU

## Slide 2
Welcome!
Ergonomics
  Heard the word before
Market products
  Toothbrushes
  Chairs
  Salsa chips?
Welcome to Introduction to Ergonomics
  SCOOPS! is a trademark of FRITO-LAY NORTH AMERICA, INC
Notes: Welcome to Introduction to Ergonomics
Welcome to Rogers Corporation Introduction to Ergonomics.
You probably have heard the word “Ergonomics” before.
Ergonomics is a word often used to market products to us these days.
You can buy ergonomically designed toothbrushes and chairs.
Did you know you can buy ergonomically designed salsa chips?
Yep, Scoops!TM are designed to not break when you dip!
Which is a good thing, otherwise the next person has to figure out how to get the broken chip out of the salsa bowl!

## Slide 3
Ergonomics is a Powerful Tool
Powerful tool
  Improve health and safety
  Improve quality and productivity
Training
  Use ergonomics to your advantage!
  Work
  Home
Notes: Ergonomics is a Powerful Tool
Well, ergonomics is also a powerful tool used in manufacturing workplaces to improve employee health and safety as well as quality and productivity.
In the Rogers Corporation Introduction to Ergonomics training, you will learn how you can use ergonomics to your advantage at work and even for activities at home.

## Slide 4
Ergonomics: Defined
Back in the day
  Bags of flour loaded
  More bags, more pay
Modern day
  Work efficiently and safely
  Design of workstations, tools, equipment and work processes
“Work smarter, not harder!”
Notes: Ergonomics: Defined
Let’s start by defining ergonomics.
Think about it this way. Back in the day, a person might have been paid by how many bags of flour they loaded.
The more bags loaded the more money they made that day!
Things have changed, now what we get paid for is working efficiently and safely, not for how much energy we expend.
Ergonomics is all about designing our workstations, tools, equipment and work processes to accomplish this.
In other words, Ergonomics means “Working smarter, not harder!”

## Slide 5
Working smarter, not harder
  Producing a quality part in a safe manner
“Working Smarter, not Harder!”
Notes: “Working smarter, not harder!”
Working smarter, not harder means producing a quality part in a safe manner.

## Slide 6
Please select the correct answer:
  Ergonomics is, “Working harder, not smarter.”
  Ergonomics is, “Working smarter, not harder.”
Quiz – What is Ergonomics?
Notes: What is Ergonomics?
Please select the correct answer:
Ergonomics is, “Working harder, not smarter.”
Ergonomics is, “Working smarter, not harder.”

## Slide 7
“Working Smarter, Not Harder”
  How can we use Ergonomics?
  Physical relationships between ourselves and work
Think about work position?
  Back, head, shoulders and arms
  Thinking . . .maybe not so good!
  Intuitively recognize issue
  Impact?
Set of ergonomics relationship principles
Ergonomics Principles and Physical Relationship
Neutral Position
Reach Zone
Power Position
Fatigue Control
Notes: Physical Relationship between Ourselves and our Work
What does “Working Smarter, Not Harder.” really mean? And how can we use Ergonomics to accomplish this?
Well, we need to consider the physical relationships between ourselves and our work.
For example, what do you think about this work position?
Look at the position of the back and the head and the shoulders and the arms. Right away you are thinking maybe not so good! You intuitively recognize this position could cause some problems.
Now we recognize exactly how this will impact different people depends on a number of factors. How long is the positioned maintained and how often and so on. Hang on to these questions, we’ll come back to them.
For right now we need to come up with a set of ergonomics relationship principles that help us accomplish our objectives of efficient and safe work. Let’s outline the ergonomics principles.

## Slide 8
Foundation of the body?
  Is it the feet?
Consider if a person sprains an ankle?
  Pair of crutches they still get around
What if person “sprains” their back?
  Significant problem even getting out of bed to get to the bathroom!
Promote Neutral Position and Support
Notes: Neutral Position: Foundation of Body
Here is a question for you.
“What is the Foundation of our body?”
Well, you might answer, “The feet!”
Makes sense, we stand on our feet. But let’s dig a little deeper. Ever know someone who had a serious ankle sprain? Could they still get around? They could with a pair of crutches.
How about someone who suffered a serious back sprain. Very likely they had a very hard time just trying to get out of bed to get to the bathroom!

## Slide 9
Neutral Position: Spine and Pelvis
Spine neutral position
S-shape (side view)
  Inward curves in low back and neck
  Outward curve in midback
Spring-like shape
  Deal with compression and shear stresses
Notes: Neutral Position: Spine and Pelvis
So, although we stand upright on our feet, we know it's really the back – the spine and pelvis - that provides the foundation for our body.
When you hold yourself in what is called the “neutral position”, your spinal column, when viewed from the side, is actually in an S-shape configuration. An inner curve in the lower back and neck and an outer curve in the mid-back area.
Why S-shape? Think springs! The S-shape allows the spine to act like a spring and increases the spine’s ability to handle stress.

## Slide 10
Limb joint “neutral position”
  Mid-range of joint position
Mid-range for elbow
  Elbow straight or bent?
  90 degrees of bend
  Greatest strength and protects joint
Mid-range of joint position
Neutral Position: Arms and Legs
Notes: Neutral Position: Arms and Legs
What about the other joints of the body? Every joint has a “neutral position”. We call it, “mid-range of joint position”.
Think about your elbow. From a physical performance standpoint, what position of the elbow is the most functional?
With the elbow straight or bent all the way?
The elbow is most functional at about 90 degrees of bend. This is the position of greatest strength and also protects the joint and surrounding soft tissues like muscles, tendons, ligaments and nerves.
Every joint of the body has a “mid-range of joint position”.

## Slide 11
100% of time in Neutral?
  NO!
15% more time?
  Mid-range of joint position
  Identify why out of neutral
  Options to change
  Work Positioner
15% Membership Club!
  Can make a big difference!
Neutral Position: 15% Club
NO!
15%
Notes: Neutral Position: 15% Club
Can you spend all of your time with your spine and joints in the absolute neutral position.
The answer is, “NO!”.
How about 15% more?
The closer you can position your joints to the “mid-range of joint position” during work tasks, the better.
The next time you find yourself in an out-of-neutral position, identify why you are out of neutral and consider options that allow you to be more in neutral.
For example, make use of a work positioner to work more in a neutral position.
Even if you can spend 15% more time in neutral, that 15% can make a big difference!
Join the 15% Club.

## Slide 12
Neutral position
  Body’s joints; spine, arms and legs
Where we use hands to do work
  How long hold 10# load at arm’s length?
  Gets heavy fast!
  Hold it as close to body as you can
Reach Zone: Arm’s Length
Notes: Reach Zone: Arm’s Length
Ok, the first principle has to do with the neutral position of our body’s joints; the spine, arms and legs.
Our second ergonomics principle has to do with where we use our hands to do our work.
For example, how long can you hold a 10# load at arm’s length?
Well, at arm's length, it gets heavy fast! That’s why, in fact, if you must hold the load at all, you know you want to hold it as close to your body as you can.

## Slide 13
Reach Zone: Operating Range
Determined by arm’s length
  Sphere from hip to mid-chest level
  Within arm’s reach to front
  About 45 degrees to side
Notes: Reach Zone: Operating Range
Structurally, the body is designed to function within a specific operating range.
We call this the Reach Zone.
Determined by your arm’ length, it’s defined by a sphere from hip to mid-chest level within arm’s reach to the front and about 45 degrees to the side.

## Slide 14
Never reach outside reach zone?
  NO!
Reaching outside reach zone
  Heavy load
  Awkward position
  Ways to decrease reach distance
Reach Zone: Operating Range
NO!
Notes: Reach Zone: Operating Range
Are we saying never reach outside your reach zone?
Of course, the answer is NO!
But if you find yourself reaching outside your reach zone with a heavy load in an awkward position, think about ways to decrease the reach distance.
In general, set up as much as possible to work within your Reach Zone.

## Slide 15
Lift or move parts, containers, equipment
  Neutral Position best position?
  As it turns out – it’s not!
Power Position
  Feet shoulder width or slightly wider
  Good footing so you don’t slip
  Spine maintained in neutral
  Hips and knees bent slightly
  Head and shoulders upright
Power Position
Notes: Power Position
So far, we have outlined the ergonomics principle of Neutral Position and Reach Zone.
But what about if you have to lift or move parts, containers, equipment, and so.
Is the Neutral Position really the best position for this kind of activity?
As it turns out – it’s not.
From the body’s perspective the third ergonomics principle, “Power Position” is a better way to go.
Here’s what the Power Position looks like:
Feet shoulder width or slightly wider
Good footing so you don’t slip
Spine maintained in neutral
Hips and knees bent slightly
Head and shoulders upright

## Slide 16
Used in just about any sport as “ready” position
  Probably have used it yourself
How about at work?
  Lifting materials
  Using tools and equipment
  Setting up work area
Used by professional weightlifters
Power Position: Sports “Ready Position”
Notes: Power Position: Sports “Ready Position”
In fact, the Power Position is used in just about any sport as a “ready” position. You probably have used it yourself when playing sports.
How about at work? You can use the Power Position in many ways – lifting materials but also, for using tools and equipment and setting up the work area.
The Power Position is the basis for the Power Lifting technique used by professional weightlifters.

## Slide 17
Power Position: Water Fountain
Drink at the water fountain!
  Rather than just bending over at waist with knees straight
  Use Power Position
  Give it a try!
Notes: Power Position: Water Fountain
You can even use the power position to get a drink at the water fountain! Rather than just bending over at the waist with your knees straight – stressing your lower back – use the power position.
Give it a try!

## Slide 18
Power Zone
  Related to Reach Zone
  Handle largest loads
Green Zone
  Mid-chest to mid-thigh level
  Close to body as possible
Yellow Zone
  Caution
Red Zone
  Avoid manual material handling
  Mechanical handling equipment
Power Position: Power Zone
Notes: Power Position: Power Zone
The Power Position includes the Power Zone. This is related to the Reach Zone and is defined as the Zone where we can handle the largest loads while lifting, carrying, pushing and pulling.
This is indicated by the GREEN Zone in the Power Zone Chart and as you might expect this is from about mid-chest to mid-thigh level and as close to the body as possible.
As you get farther away from the GREEN Zone, it becomes YELLOW; in this zone, please recognize our body cannot handle as heavy a load. Exercise caution. Ensure your technique is good and consider getting help or using a lifting device.
The farthest away zones are in RED. Try very hard to avoid any manual material handling in these zones. Mechanical handling equipment is strongly recommended.

## Slide 19
Fatigue Control at Work
Fatigue Control at work
  Word “Control” and not “Eliminate”
  Physical fatigue is normal occurrence
  Not possible to eliminate fatigue
  Recognize and control effects of fatigue
Personal Health and Wellness
  Recover from day’s fatigue
  Rest, hydration, nutrition and exercise when not at work
Notes: Fatigue Control at Work
So far, we have covered the ergonomics principles of Neutral Position, Reach Zone and Power Position with the Power Zone. The last principle is personal Fatigue Control at work.
You’ll notice we’re using the word “Control” and not “Eliminate” when discussing fatigue. Physical fatigue is a normal occurrence in the routine of our lives. It is not possible to eliminate fatigue. Our goal is to understand how to recognize and control the effects of fatigue throughout the workday.
Also, for overall personal health and wellness, we need to recover from the day’s fatigue through appropriate rest, hydration, nutrition and exercise when we are not at work to get ready for the next day.

## Slide 20
Recognize fatigue at work?
  Muscle tiredness
  Decrease in general physical strength and coordination
  Make mistakes
  May be more likely to experience injuries
Fatigue Control: Recognize Fatigue
Notes: Fatigue Control: Recognize Fatigue
First, how do you recognize fatigue at work?
Physical fatigue is demonstrated when physical and/or repetitive tasks result in muscle tiredness.
We may experience a decrease in general physical strength and coordination.
We are more prone to making mistakes.
We may be more likely to experience injuries.

## Slide 21
Control fatigue?
  Mix up job tasks
  Breakup larger task into smaller tasks
  Drink plenty of fluid
  Appropriate recovery breaks during shift
  Replenish energy supplies
  Stretching to promote blood circulation and joint lubrication
  15 to 30 second micro-stretch breaks
Fatigue Control: Strategies
Notes: Fatigue Control: Strategies
What can you do to control fatigue?
Try to mix up job tasks to provide a variety of physical activities. This is called job rotation. As possible breakup a larger task into smaller tasks.
Drink plenty of fluid on a periodic basis. If you are thirsty, you are on the way to dehydration.
Make sure you take appropriate recovery breaks during the shift to give your body a chance to replenish energy supplies. Nutrition makes a difference.
Use stretching to promote blood circulation and joint lubrication through-out the shift. Stretching with the stretch group makes good sense.
Also take 15 to 30 second micro-stretch breaks throughout the shift.

## Slide 22
Quiz: Fatigue Control Strategies
Please select strategies you can use to help control fatigue at work:
Drinking enough water to prevent dehydration.
Maintaining adequate nutrition to fuel your body throughout the shift.
Ignoring the physical effects of fatigue throughout the shift.
Performing “Micro-Break Stretches” throughout the shift.
Notes: Quiz: Fatigue Control Strategies
Please select the strategies you can use to help control fatigue at work.
Drinking enough water to prevent dehydration.
Maintaining adequate nutrition to fuel your body throughout the shift.
Ignoring the physical effects of fatigue throughout the shift.
Performing “Micro-Break Stretches” throughout the shift.

## Slide 23
Efficiency of Movement
  Neutral Position
  Reach Zone
  Power Position
  Fatigue Control
Ergonomics Factors
  Force
  Posture
  Repetition
Efficiency of Movement and Ergonomics Factors
Neutral Position
Reach Zone
Power Position
Fatigue Control
Force
Repetition
Posture
Notes: Efficiency of Movement: Primary Ergonomics Factors
Neutral Position, Reach Zone, Power Position and Fatigue Control are all tied together to create what we call, “Efficiency of Movement”. What is “Efficiency of Movement”?
To answer that question, along with the Ergonomics Principles, we need to add three interrelated primary Ergonomics Factors of Force, Posture and Repetition.

## Slide 24
Handling heavier part
  Force: level of physical effort
Level of muscular effort depends on
  Height and distance of part from you
Power Zone
  Within Power Zone – more force
  Away from Power Zone – less force
Primary Ergonomics Factors – Force
Notes: Primary Ergonomics Factors – Force
Imagine you are handling a heavier part.
In this case, the Force is the level of physical effort your muscles need to produce to handle the part.
As we discussed in the Reach Zone and Power Position sections the level of muscular effort depends on far away the load is from you both in terms of height and distance.
The more you are working within the Power Zone the more force you can produce and conversely the farther away from the Power Zone the less force you can produce.

## Slide 25
Posture Ergonomics Factor
  Directly related to Neutral Position Ergonomics Principle
  More neutral . . . less potential for stress
Improve position of body, arms and legs
Primary Ergonomics Factors – Posture
Notes: Primary Ergonomics Factors – Posture
The Posture Ergonomics Factor is directly related to the Neutral Position Ergonomics Principle.
The more neutral the posture is . . . the less stress on the body and limbs.
That is why in Ergonomics we work hard to improve the position of our body, arms and legs.

## Slide 26
Repetition
  How often (frequency)
  How long (duration)
  Exposure to factors of Force and Posture
Without breathing for 30 to 60 seconds
  Without any serious consequence
Lack of oxygen for five or six minutes?
  No oxygen for body and particularly brain
  Leads to very serious consequence!
Primary Ergonomics Factors – Repetition
Notes: Primary Ergonomics Factors – Repetition
Repetition is the third primary Ergonomics Factor. Essentially it is how often (frequency) and how long, (duration) the task is occurring.
Really, we are talking about the level of exposure to the factors of Force and Posture.
For example, most people can go without breathing for 30 to 60 seconds without any serious consequence. How about a lack of oxygen for five or six minutes?
That level of exposure with no oxygen for the body and particularly the brain leads to a very serious consequence!

## Slide 27
Force, Posture and Repetition are inter-related
Scoring system – each Factor score of 1 to 10
  1 is not an issue
  10 is a big problem
For particular task each Factor gets score of 10
  10 times 10 times 10 is 1000
  Cumulatively, pretty high score!
Primary Ergonomics Factors – Inter-related
10 x 10 x 10 = 1000
Force
Repetition
Posture
Notes: Primary Ergonomics Factors – Inter-related
You are probably getting the message that Force, Posture and Repetition are all inter-related.
Think about it this way. Let’s put a scoring system in place where we give each Factor a score of 1 to 10 where 1 is not an issue and 10 is a big problem. For a particular task we examined, each Factor gets a score of 10.
10 times 10 times 10 is 1000. So cumulatively we have a pretty high score!

## Slide 28
Ergonomics improvement
  Reduce Force and Posture Factors to 7 out of 10
  Can’t reduce repetition rate
  Repetition remains at 10
Repeat calculation
  7 times 7 times 10 is 490
Moderately improving Force and Posture scores
  Reduce overall physical impact by more than 50%!
Primary Ergonomics Factors – Inter-related
7 x 7 x 10 = 490
Force
Repetition
Posture
Notes: Primary Ergonomics Factors (7 X 7 X 10 + 490)
Let’s say we can make ergonomics improvement that reduce the Force and Posture Factors to 7 out of 10. In many cases these changes can be fairly straight-forward to make. But let’s say we really can’t reduce the repetition rate. We still need to produce the quantity of parts needed. So, repetition remains at 10.
Repeating our calculation:
7 times 7 times 10 is 490.
Wow, by moderately improving the Force and Posture scores we can reduce the overall physical impact by more than 50%!

## Slide 29
Repetition is called “Great Multiplier”
  Magnifies impact of Force and Posture factors
  One time, probably not a big deal
  Same task repeated can add up!
Manufacturing processes
  Same series of repetitive physical movements
  Control Primary Ergonomics Factors
Efficiency of Movement: How it Works?
Notes: Efficiency of Movement: How it Works?
How does this relate to Efficiency of Movement? Repetition is called the “Great Multiplier” because it magnifies the impact of the Force and Posture factors on the body. Perform it one time, probably not a big deal but the same task repeated a hundred times can add up!
Many of the manufacturing processes at Rogers Corporation are repetitive in nature. A certain quantity of parts need to be machined, fabricated and so on. The same series of repetitive physical movements are required to complete the task. That is why it is so important to work on controlling the Primary Ergonomics Factors of Force and Posture to the highest level possible.

## Slide 30
Efficiency of Movement: Habits are Important
Two people do same task
  One person makes it look so easy
  Other person seems to really struggle
What is the difference?
  Efficiency of Movement
  One person has very efficient physical movement habits
  Other person’s habits are not efficient
Notes: Efficiency of Movement: Habits are Important
Have you ever watched two people do the same task, one person makes it look so easy and yet the other person seems to really struggle? What is the difference? Well, that is we call Efficiency of Movement.
One person has developed a set of physical movement habits that are very efficient while the other person has also developed a set of physical movement habits, but they are not efficient. Why?

## Slide 31
Efficiency of Movement: Physical Activity – Golf
Learn how to play golf
  Golf lessons to learn basics of how to swing a club
Start to practice
  One person has beautiful swing
  Other person, not so good
What happened?
Notes: Efficiency of Movement: Physical Activity – Golf
Let’s say a person wants to learn how to play golf; it doesn’t have to be golf – it could be any physical activity. But let’s use golf as our example.
Both go get some golf lessons to learn the basics of how to swing a club. They both start to practice and in a few weeks one person has a beautiful swing and drives the ball 200 yards down the fairway.
The other person, not so good. They have developed a bad hook and can’t seem to correct it even with additional instruction. What happened?

## Slide 32
“Motor Skill”
  Brain tells body what to do
  Muscle and nerve connections created between brain and muscles
  Feedback from muscles to brain
Developing habits
  Smooth swing
  Hook
Both developed muscle and nerve connections
  One set was efficient and the other was not
Efficiency of Movement: Motor Skill
Notes: Efficiency of Movement: Motor Skill
Swinging a golf club is what is called a “motor skill”. The brain tells the body what to do and as the person practices the swing there literally are a series of muscle and nerve connections created between the brain and the muscles. There is also feedback from the muscles to the brain. It is a two-way street.
Both of our golfers were developing habits about how to swing the club. One had developed habits that resulted in a smooth swing and the other developed habits that resulted in the hook. Both developed the muscle and nerve connections; just one set was efficient and the other was not.

## Slide 33
Habit is particularly good one or bad one
  We get used to it
“Large Functional Reserve”
  Physically tolerate large amount of physical stress and seemingly be ok
  Accommodate to physical activities
Push close to threshold of physical stress
  Beyond threshold, tissues can fail very quickly
Efficiency of Movement: Accommodation
Functional Reserve
Notes: Efficiency of Movement: Accommodation
At work and home, whether the habit we develop is a particularly good one or a bad one, we simply get used to it ; we accommodate to it.
We have what is called a “large functional reserve”. What that means is that we can physically tolerate quite a large amount of physical stress and seemingly be ok.
We know that our bodies have a great ability to accommodate to whatever physical activities we are doing.
With our “functional reserve” we can push very close to a threshold of physical stress into muscles, tendons, ligaments, nerves and other tissues of the body where beyond that threshold the tissue can fail.
But once we cross that threshold the tissues can fail very quickly.

## Slide 34
Shoveling snow by hand
  Wet and heavy
Existing narrowing of arteries supply blood to heart muscle
  Initially everything goes ok
  Heart muscle can’t get enough oxygen
  Heart attack!
Soft tissue injuries
  Back disc problems
  Tendonitis
  Muscle sprains
Efficiency of Movement: Accommodation
Notes: Efficiency of Movement: Accommodation – Medical Analogy
Here is a medical analogy. Imagine its wintertime and a person is out shoveling snow by hand. The snow is wet and heavy, and the person is working hard.
Now, let’s say the person has an existing narrowing of the arteries that supply blood to the heart muscle. Initially everything goes ok, but then they cross the threshold where the heart muscle can’t get enough oxygen and you know what the result can be.
Heart attack!
Failure occurs very quickly. We know this same process can take place with soft tissue injuries like back disc problems, tendonitis and muscle sprains.
What can we do?

## Slide 35
Practice is important to get proficient
  Practiced same amount of time
  How they practiced made difference
Vince Lombardi (Green Bay Packers football coach)
  “Practice doesn’t make perfect. Only perfect practice makes perfect.”
Establish muscle nerve connections
  Unless practice is perfect get very good at doing it wrong!
Perfect Practice makes Perfect!
Notes: Efficiency of Movement: Perfect Practice makes Perfect!
Well, we all know that practice is important to get proficient . Well, both “golfers” practiced the same amount of time. How they practiced made all the difference.
Vince Lombardi, the legendary Green Bay Packers football coach said it well.
“Practice doesn’t make perfect. Only perfect practice makes perfect.”
He understood that you can practice over and over again, and you will establish those muscle nerve connections we talked about, but unless your practice is perfect you will get very good at doing it wrong!

## Slide 36
Practice that develops good habits
  Efficient and safe
Ergonomics plays huge role
  Ensure workstations, tools and equipment
  Well designed
  Work habits fall in line with ergonomics principles
    Neutral Position
    Reach Zone
    Power Position
    Fatigue Control
We want Efficiency of Movement!
Efficiency of Movement: In the Groove!
Neutral Position
Reach Zone
Power Position
Fatigue Control
Notes: Efficiency of Movement: Practice at Work
Efficiency of Movement is all about practice that develops the good habits that we need to be efficient and safe in what we are doing.
That’s where ergonomics plays a huge role. With ergonomics we want to ensure the workstations, tools and equipment are well designed and that the work habits we develop fall in line with the ergonomics principles of Neutral Position, Reach Zone, Power Position and Fatigue Control.
We want to establish the muscle nerve connections that result in efficient and safe work activities. We want Efficiency of Movement!

## Slide 37
Can less efficient person change to become more efficient?
YES!
Understand
  How muscle nerve connection process works
  Identify habits to change
Possible to change old troublesome habits into new efficient habits
  Takes work and time
  Appropriate workstation, tools and equipment ergonomics
“Teach an old dog new tricks!”
Efficiency of Movement: Change Habits?
YES!
Notes: Efficiency of Movement: Change Habits?
You probably are thinking right about now – can the less efficient person change to become more efficient?
Well, the answer is a resounding. YES!
With an understanding of how the muscle nerve connection process works and identifying what habits you want to change; it is possible to change old troublesome habits into new efficient habits. It takes work and time, and it does involve making sure the ergonomics of the workstation, tools and equipment are appropriate.
But yes, it is possible to “Teach an old dog new tricks!”

## Slide 38
Quiz: Change Habits
It is possible to change bad old habits into better new habits.
True
False
Notes: Change Habits
It is possible to change bad old habits into better new habits.
True
False

## Slide 39
Concepts of Ergonomics
  Neutral Position
  Reach Zone
  Power Position
  Fatigue Control
  Efficiency of Movement
Person who Practices Ergonomics
  Called an Ergonomist
“Who are the best Ergonomists?”
Neutral Position
Reach Zone
Power Position
Fatigue Control
Best Ergonomist!
Notes: Best Ergonomist!
Now that you have a handle on the ergonomics principles of Neutral Position, Reach Zone, Power Position and Fatigue Control and the Efficiency of Movement concept, let’s pull it all together.
A person who practices Ergonomics is called an Ergonomist.
Here is a question for you, “Who are the best Ergonomists?”

## Slide 40
Who are the experts in your job?
Best Ergonomist!
  You are experts in your jobs!
  Collaboration with stakeholders
  Everyone’s work is safer and more efficient!
Thanks for your time and attention!
Notes: Best Ergonomist!
One way to answer this question is to ask another one, “Who are the experts in your job?”
Experience tells us you are the experts in your jobs; you do them day in and day out and you know all the details.
So, doesn’t it make sense that the best people to make use of the Ergonomics Principles are the experts in the jobs?
On an on-going basis, you, collaborating with your Group Leads, Management, Union, Health and Safety, Engineering and all the other stakeholders continue to make everyone’s work safer and more efficient.
Thanks for your time and attention.

## Slide 41
Menu
Title
Welcome
Ergonomics Defined
Ergonomics Principles
  Neutral Position
  Reach Zone
  Power Position
  Fatigue Control
Efficiency of Movement
  Ergonomics Factors Inter-related
  Efficiency of Movement: How it Works
  Habits
  Accommodation
  Practice Makes Perfect
Best Ergonomist
Menu
Notes: Menu