## Slide 1: WorkWell and ErgoSystems Present:
Office Ergonomics
for Health Care Professionals
WorkWell Systems, Inc.
ErgoSystems Consulting Group, Inc.

## Slide 2: Welcome!
Objectives
Discover what Office Ergonomics is all about
Identify components that make up the successful office workspace
Learn how to analyze and setup the office workplace
Acquire confidence in using system through practice

## Slide 3: Workshop Guidelines
Follow along with demonstrations unless you think they may cause you a problem
Do not go against doctor's orders or do anything that you feel you should not
If you are uncomfortable sitting during workshop, move to side or rear of classroom
Use your good judgment when trying new techniques or exercises after you leave workshop

## Slide 4: Course Logistics
Manual/handouts
Course Schedule
  Starting/ending times
  Rest breaks
Rest rooms
Fire exits
Telephones
Messages
Group Introductions

## Slide 5: It’s all about relationships!
The relationships we form are one very important part of life
In office ergonomics, relationships between the user and the chair, workstation and equipment are also a critical component

## Slide 6: Relationships
What do you see as potentials problems in this example?

## Slide 7: Discovery
You already know a good deal about office ergonomics!
You really can’t tell a whole lot until you see the workspace in use!

## Slide 8: Office Ergonomics Applications
Typewriters to computers!
Where do we use computers?
EVERYWHERE!

## Slide 9: Typical office components
User population profile
User – Single/Multi
Tasks – Single /Multi
Floor space
Seating system
Worksurface
Floor surface
Computer equipment
Telephone
Office equipment
Storage
Conference tables/chairs
Light
Noise
Temperature

## Slide 10: User population profile
Very important first step - accurately define user population
  Age
  Gender
  Stature
  Vision
  Hand dominance
  Other
Defining user profile lays the foundation for remainder of process

## Slide 11: User –Single/Multi

## Slide 12: Single user
Less influenced by need for adjustability of workstation itself
Once determine proper height of worksurface
  Use fixed height or adjustable/fixed worksurface
  Worksurface can be height adjusted but once adjusted is not readily changed

## Slide 13: Multi user
Multi-user workstations require significantly greater degree of adjustability
Critical that changeover from one user to next accomplished quickly and easily
Adjustable/adjustable worksurface
  Through spring balanced manual system/powered system worksurface height readjusted within seconds

## Slide 14: Tasks: Single-task or Multitask

## Slide 15: Single-task
Majority of work time accomplishing specific focused task
For example, customer service representative majority of day on computer and telephone performing computer lookup activities
Physically job demands are concentrated in single area
Efficient set up is critical because user tends to maintain sustained position to perform activities

## Slide 16: Multi-task
Number of different tasks need to be accomplished
  Computer
  Telephone
  Writing workstation
  Attending meetings
  And so on

## Slide 17: Work Activity (percentage breakdown)
Computer
Telephone
Read
Write
Meetings
Misc
Other

## Slide 18: Floor space
In ideal world, dimensions of office workstation are determined exclusively by job tasks
  Some very focused single-task workstations 48 sq ft
  Multitask workstation 120 sq ft or even more

## Slide 19: We do not live in an ideal world
Floor space may be determined by host of factors not relative to job task
Does not negate need to perform an effective job analysis to make recommendations
Does cause us in many cases to be quite creative!

## Slide 20: Office Ergonomics Workstation Evaluation Form

## Slide 21: Office Ergonomics Workstation Evaluation Form
Background Information
Demographics
Work Activity
Reason for assessment

## Slide 22: Chair
Objectives of chair
  Support body and limbs to provide relief from weight bearing
  Provide stable base or platform for body and limbs
  Position user at correct height and reach relationship to worksurface and tasks at hand
  Allow for easy change in position/movement of user

## Slide 23: Types of seating systems
Number of seating systems available in workplace
  Office chairs
  Stools
  Lean platforms
  Other miscellaneous seating

## Slide 24: Chair criteria
Type, use and efficiency of chair are critical elements
Acceptable chair criteria determined by:
  Type of job activities performed
  Size and shape of user
  Duration of time spent in chair

## Slide 25: Legs and Casters
Does the chair have at least 5 legs?
Does the chair roll easily on the floor surface?
  Hard caster on soft floor
  Soft caster on hard floor

## Slide 26: Seatpan Height
Does the chair’s seatpan height adjust up and down?

## Slide 27: Seatpan Tilt
Does the chair’s seatpan tilt up and down?

## Slide 28: Seatpan Tension
Can you adjust the seatpan tension?

## Slide 29: Seatpan Depth
Does the chair’s seat move forward or backward?

## Slide 30: Seatpan Fit
Does the chair’s seat fit body size?

## Slide 31: Relationships
Does the chair fit the individual?
  This gentleman is 7’ tall!
  Arrows point to back of knee and front edge of seatpan

## Slide 32: Back Support Height
Does chair’s back support move up and down?

## Slide 33: Back Support Angle
Does chair’s back rest angle forward or backward?

## Slide 34: Cushion
Suitable cushion
  Foam density
  Wearability
  Breathability
  Type of material (fabric or rubberized)

## Slide 35: Armrests Adjust
Do chair’s armrests adjust up and down and/or side-to-side?

## Slide 36
Relationships

## Slide 37: Maintenance
Is chair functioning properly?
No maintenance problems?

## Slide 38: Adjustment levers/knobs/controls
Easy to reach
Easy to manipulate
Should not intimidate

## Slide 39: Ball Chairs?
Therapeutically, exercise balls used in clinical settings as treatment modalities
  Improve spinal stability
Over past several years, use of exercise balls in place of or in addition to task chairs
  Currently only anecdotal evidence exists to support full-time use
Most ergonomists advocate for properly sized/properly adjusted office task chairs rather than use of ball chairs

## Slide 40: Art of Sitting
Body not designed to sit
  Particularly for long periods
  Studies determined even when seated in well-supported postures . . .
  How soon do we want to move?
  About every 20 to 30 minutes!

## Slide 41: The Art of Sitting
Three point contact
  Sacrum/Trunk
  Hips/Thighs
  Feet/Floor

## Slide 42: The Art of Sitting
90/90 seated posture?
  Only in drawings!
  Most people will sit at 95 to 110 degrees at hips and knees

## Slide 43: Sitting styles
Sitting styles quite varied from person to person:
  Percher
  Slouch
  Sit crossed leg
  Sit on leg

## Slide 44: Sitting styles
Particular sitting style needs to be assessed
  Habit developed over time
  Response to poor workstation setup
  Combination of both
  What drives problem is frequency and duration of seated position

## Slide 45: Functional seated positions
Provide for several different acceptable postures
Rotate throughout day on regular basis:
  Upright “keyboard” position
  Semi-reclined/rocking “conversation” position
  Standing

## Slide 46: Adjustment anxiety
Chairs can be pretty expensive
  All kinds of bells and whistles
  Chair only as good as how it is adjusted
Some people have never adjusted their chair
  Just sit down and go to work!
Bottom line
  Need to initially be able to adjust chair to fit
  As well as throughout day

## Slide 47: Chair solutions
Manual
  Find and read it!
Position and support body in neutral
  Adjust seat pan/back support tension to hold body in neutral position
  Adjust seatpan height to get feet on floor with even pressure on hips and thighs
  Adjust height and angle of back support to fill in low back curve

## Slide 48
Relationships

## Slide 49: Chair

## Slide 50: MOVE!
Remember, no matter how perfectly adjust chair to fit
  Still comes down to fact that need to move on regular basis to keep body healthy and safe
Movement is critical to the health of the body!

## Slide 51: Worksurface
Worksurface objectives
  Provide functional workspace (depth, width)
  Support and position equipment
  Provide access to work materials
  Achieve desired relationship match between user/work

## Slide 52: Straight line (desk/table)
The straight in-line configuration is suited for single task activities with minimal reach requirements for other office equipment and materials

## Slide 53: L-shape (two worksurfaces)
L-shaped configuration is suited for single to multitask activities that require two or more separate workspaces
One workspace may be used as computer workstation and another as writing or collating workstation

## Slide 54: Corner/U-shaped
Corner/U-shaped configuration well suited for multitask activities in same workspace with significant requirements to frequently reach other office equipment and materials
Allows for greatest degree of adjustability and accommodation for user

## Slide 55: Worksurface Fixed
Traditional desk at fixed worksurface height of 29 inches - Millions of these!
Not designed to be changed in height or angle
Generally possible to raise fixed height worksurface on supports but also generally very difficult to lower it

## Slide 56: Worksurface Fixed/Adjustable
Wall panel mounted worksurface or worksurface on legs
Can be adjusted within given range but once adjusted fixed in that position on fairly permanent basis

## Slide 57: Adjustable/adjustable
Sit/stand workstations
  Controlled by mechanical springs or powered mechanisms
Keyboard trays
  User can readily and easily adjust worksurface

## Slide 58: Wrong Desk height
If work height is adjustable, adjust it as needed
  Raise height of work surface by putting it up on blocks
  Make sure desk or work surface is solidly placed on blocks and won’t fall off!
Adjust chair height
  Make sure feet are supported either on floor or with footrest
Add height/angle adjustable keyboard tray
  Mounted underneath work surface

## Slide 59: Not enough layout space
House cleaning
Other worksurfaces available for use
  File cabinet at standing height to review documents
Relocate some of equipment on desk
Pullout drawers already in desk

## Slide 60: Sit/Stand Workstations
Worksurface at standing height
Stool
Foot rest

## Slide 61: Sit/Stand Workstations
Portable system placed on desk
  Adjustable keyboard/mouse and monitors
  Use chair when seated

## Slide 62: Sit/Stand Workstations
Height adjustable sit/stand workstation

## Slide 63: Worksurface

## Slide 64: Foot Support
In an ideal world the best foot support when seated in a chair is the floor . . .
However if needed use proper sized foot rest

## Slide 65: Knee/foot clearance
Move what is not needed to some other storage position or get rid of it
Survey work area and determine what is blocking access

## Slide 66: Foot Support/Clearance

## Slide 67: Sharp edges
Proper work height in relation to worksurface edge
  Many times will eliminate the issue
Pad sharp edge
  If cannot eliminate pad the edge

## Slide 68: Work organization
Includes organization and structure of tasks/activities performed throughout workday
  e.g. Do not store file boxes on the floor

## Slide 69: Work organization solutions
Space in most companies is premium
  Store infrequently used items outside of immediate work environment
Pick up at end of day

## Slide 70: Floor surface
Providing ease of rolling chair on floor surface
Nonskid surface to prevent slips and falls
Non glare surface to reduce overall glare in workstation

## Slide 71: Computer equipment

## Slide 72: Keyboards
Keyboard configurations
  Straight-line
  Curved
  Articulated
Keyboard surface finish
Keyboard size
Keyboard activation pressure
Layout
Wireless

## Slide 73: Keyboard Technique
Use of worksurface for forearm support
Free float piano playing style

## Slide 74: Non-neutral Keyboard Positions

## Slide 75: Keyboard Solutions
Based on technique obtain correct height, reach and angle of keyboard
Adjust keyboard height and position
  Adjust worksurface height
  Keyboard tray
If cannot adjust keyboard height, position chair height to place hands in neutral posture in relation to keyboard
  May require support for feet if no longer touch floor

## Slide 76: Wrist rests
To use or not to use . . .
That is the question!

## Slide 77: Poor Technique
If technique needs improvement
Training programs that teach improved technique

## Slide 78: Take break
Add stretching to day
  A little post it note put on computer monitor
  Software that reminds you to stretch
  Old-fashioned as egg timer
  Team up with someone else in office
  Take advantage of natural breaks between activities
Remember to Stretch!

## Slide 79: Keyboard Trays
Keyboard tray configurations
Keyboard tray size
Height adjustment
Angle adjustment
Knee clearance

## Slide 80: Keyboard Tray

## Slide 81: Keyboard

## Slide 82: Pointing device
No not that kind of mouse!
Use mouse as little as possible
  Keyboard shortcuts

## Slide 83: Pointing device technique
Neutral positions
  Same plane as keyboard
Mousing style or technique
  Free float piano playing style
  Use of worksurface for forearm support

## Slide 84: Pointing Device Non-neutral Positions

## Slide 85: Mouse Wrist Rests
In most cases, mouse wrist rest is not recommended
  Wrist rest tends to “anchor” wrist
  Excessive side-to-side deviation of hand
Straight in access
  Allow forearm, wrist and hand moving as unit to manipulate mouse
  Think of mouse as extension of arm NOT just extension of wrist

## Slide 86: Pointing Device Solutions
Based on technique
  Adjust worksurface height
  Mouse tray
Cannot adjust mouse height and position
  Position chair height
  May require foot support
Keyboard shortcuts
Zoom with CTRL/SCROLL WHEEL

## Slide 87: Choosing Correct Pointing Device

## Slide 88
Mouse Setup
Buttons
Pointers
Pointer Options
Wheel
Hardware

## Slide 89: Mouse

## Slide 90: Computer
Where?
  Computer underneath monitor
  May or may not be appropriate
  Don’t block ventilation
  On/off and disc drives access

## Slide 91: Relationships

## Slide 92: Computer

## Slide 93: Monitor
Everything need access to may be viewed through monitor
Watch people looking at their monitors
  Almost like monitor is a vacuum cleaner
  They turn it on . . . and it sucks their head right in!

## Slide 94: Monitors
LCD
Factors
  Physical size
  Resolution
  Display size
  Colors
  Brightness
  Viewing angle

## Slide 95: Monitor Alignment
Directly face primary work task
  Primarily data creation or manipulation
    Monitor directly in front
  Primarily data entry - main focus on paper documents
    Monitor slightly off to side
    Copy stand to place paper documents directly in front

## Slide 96: Glare
Unwanted light directed or reflected into eyes
Sources
  Overhead lights
  Task lights
  Outside light
  Any shiny surface
  Any white/bright object

## Slide 97: Control Glare
First step
  Identify glare source
Control
  Control source
  Control path

## Slide 98: Use glare screen
Get what you pay for
  Inexpensive glare screen is generally just wire mesh
  Will cut glare at expense of character quality
  Good quality optical glass glare screen
Don’t have light source such as window directly behind monitor
  Reposition monitor
  Shade window

## Slide 99: Adjust monitor screen brightness and contrast

## Slide 100: Monitor Resolution
Pixel (picture element)
  640 by 480
  800 by 600
  1024 by 768
  1600 by 1800
Guideline
  Set LCD monitor resolution to the native resolution
  Typically the highest it will go

## Slide 101: Monitor Height
Where do we naturally read?
We read looking out and down

## Slide 102: Monitor Height
Top of screen no higher than eye level
Look out and use downward eye movement to look at lower part of screen

## Slide 103: Monitor too high
If screen too high
  Forces eyes wider open than usual
  Less tearing - eyes become more dry
  Tip head back putting additional strain into neck and shoulders
  Solutions
  Lower monitor
  Raise chair
  Lower worksurface

## Slide 104: Monitor too low
If screen too low
  Head forward
Solutions
  Adjust monitor stand – if adjustable
  Monitor stands/Risers
  Monitor arms

## Slide 105: Monitor Distance
Eyes
  Accommodation Convergence
Guideline
  Get screen as far away from user as possible
    At least arm’s length
    Still be able to read it clearly with good posture

## Slide 106: Monitor too far away
Slide screen towards user

## Slide 107: Monitor too close
Reconfigure monitor placement on desk
Add keyboard tray
At minimum push chair back from worksurface to give eyes a break

## Slide 108: Dirty monitor screens
On regular basis clean monitor screen
Only use approved cleaning measures

## Slide 109: Dual Monitors
Primary/Primary
Primary/Primary

## Slide 110: Dual Monitors
Primary/Secondary
Primary/Secondary

## Slide 111: Eye Examinations
Regular eye examinations
Eyewear prescriptions changes
Eye health in general
Based on job task

## Slide 112: Presbyopia
Age-related process
Slow loss of flexibility within lens inside eye
Result maybe head tip
Solutions
  Bifocals
  Computer glasses
  Progressive lens
  Lower monitor

## Slide 113: Monitor

## Slide 114: Document holder
Horizontal vs. inclined

## Slide 115: Document holders
Landscape
Portrait
Read Write Stand

## Slide 116: Document Holder

## Slide 117: Laptops
Design violates basic ergonomic principles
Fixed position keyboard and monitor

## Slide 118: Occasional Laptop User
Occasional Users
  Better off sacrificing neck posture rather than wrist posture
Find comfortable chair
  Position in lap or on table for most neutral wrist posture that you can achieve
  Angle laptop screen so can see with least amount of neck deviation

## Slide 119: Full-time Laptop User
Use separate keyboard/mouse
Port replicator/docking station
Position on desk/worksurface to see screen without bending neck
Elevate off desk surface using stable support surface, such as computer monitor pedestal
Follow postural guidelines for working at computer workstation
Transport with bag or wheeled cart

## Slide 120: Telephone
Frequency and duration
  More than 1 to 2 hours/day
  More than 1 to 2 minute calls
  Should have hands free to operate equipment

## Slide 121: Telephone Types
Handsets
  Awkward head, neck and arm position
Shoulder cradle
  Still have awkward head, neck and arm position

## Slide 122: Telephone Types
Headsets
  Wireless
  Bluetooth

## Slide 123: Telephone

## Slide 124: Handwriting/Reading
Use good old pen and paper
The paperless office?

## Slide 125: Solutions
Inclined
  Document stand or podium
Gripping
  Is it really true, harder you squeeze more ink will come out?

## Slide 126: Office equipment
Make use of principles to position office equipment
  Calculator
  Printer
  Fax
  Writing utensils
  Scissors
  Paper clips
  Stapler
  Stuff

## Slide 127: Relationships

## Slide 128: Storage/Reach zone
Primary
  Frequently accessed from seating system
  Within easy reach
Secondary
  Occasionally accessed
  Located in gray zone
  Danger Zone!
Tertiary
  Very occasionally accessed
  Have to get up and move to access

## Slide 129: Storage
Storage types
  Vertical storage racks
  Horizontal storage bin
  Wall hanging storage
File cabinet types
  Vertical
  Lateral
  Rolling
Don’t overfill
  50 files in cabinet that holds 30!

## Slide 130: Storage
Don’t overfill
  50 files in cabinet that holds 30!
Purge on regular basis
Position commonly accessed file in suitable reach zone

## Slide 131: Storage

## Slide 132: Conference rooms
How to enhance audience reception of information
Lack of physical movement
132

## Slide 133: Conference Rooms
Look for as many opportunities as possible to move as part of meeting
  Standing mixed in with sitting
Bring in small footrest or back cushion
133

## Slide 134: Lighting – General and Task

## Slide 135: Light solutions
Too much
  Turn out lights
Too little
  Add overhead lights
    Add indirect lights
    Bounce light off of ceiling and walls
  Add task light
    Desktop or wall panel lamp
    Position light carefully
Lighting Design

## Slide 136: Illumination

## Slide 137: Noise
Office can be noisy place
Contributing factor to fatigue and general stress
Noise level
  Too much noise
  Too little noise
Noise source
  Figure out where noise is coming from

## Slide 138: Control Noise
People noise
  Limit volume and length of conversations
  Make good use of more public areas or conference rooms
Equipment noise
  Move equipment
  Noise enclosures
  White noise

## Slide 139: Temperature
Never agree on same temperature!
We have different “internal thermostats”
  Too hot!
  Too cold!

## Slide 140: Temperature solutions
Survey group
  General consensus
Controls
  Window shade
  Sweater
  Personal fan

## Slide 141: Recommended Specifications

## Slide 142
Follow-up

## Slide 143: Office Ergonomics Assessment Guidelines

## Slide 144: Assessment Steps
Background Information
Job Tasks
Chair
Worksurface
Computer and Office Equipment
Environmental Factors
Recommended Workstation Setup and Specifications
Summarize Issues and Recommendations
Follow-up

## Slide 145: Ergonomics – A Potent Tool!
Great number of factors enter into the office ergonomics workplace
Use the principles and ergonomics analysis process to offer solutions that are practical and effective!

## Slide 146: THANKS!

## Slide 147: WorkWell and ErgoSystems Present:
Office Ergonomics
for Health Care Professionals
WorkWell Systems, Inc.
ErgoSystems Consulting Group, Inc.