## Slide 1: WorkWell Prevention and Care and ErgoSystems Present
Office Ergonomics: Introduction for Health Care Professionals (Online)
WorkWell Prevention and Care
ErgoSystems Consulting Group, Inc.
MENU

## Slide 2
Office Ergonomics: Introduction for Health Care Professionals
  Critical Ergonomics tool to enhance
    Safety
    Productivity
  Detailed framework
    Conduct office ergonomics assessment
    Generate reasonable and feasible recommendations
Welcome

## Slide 3
Manual/Handouts
Workshop Schedule
  Starting/ending times
  Breaks
Rest rooms
Fire exits
Telephones
Messages
Workshop Logistics
3

## Slide 4
Describe successful office workspace . . .
What do you want to accomplish?

## Slide 5
Look carefully at the words
Do you see any pattern or trend?
Is there a predominant theme?
A careful examination

## Slide 6
Look carefully at the words
Do you see any pattern or trend?
Is there a predominant theme?
A careful examination

## Slide 7
Words like comfort or comfortable mixed in with:
  Productive
  Efficient
  Satisfying
  Effective
  Safe and so on
Comfort . . . direct positive relationship to other descriptors
In other words . . .
  Comfortable
  Productive
  Efficient
  Satisfying
  Effective
  Safe

## Slide 8
The answer is NO!
Maximizing comfort can be very dangerous thing to do
Optimize comfort the in office workplace!
Maximize comfort?

## Slide 9
Focusing patient’s treatment plan
  Ergonomics analysis of patient’s work and/or home demands
Identifying potential job modifications
  Assist patient in Return to Work (or other activity) process
Preventing potential injuries to employees
  Proactive ergonomics analysis and intervention
Enhancing company’s bottom line
  Ergonomics related improvements in quality and productivity that also complement health and safety
Other?
Health Care Professionals (HCP) Advantages

## Slide 10
Discover what Office Ergonomics is all about
Identify components that make up the successful office workspace
Learn how to analyze and setup the office workplace
Acquire confidence in using system through practice
Workshop Objectives

## Slide 11
At the end of training, participants will be able to
  Describe physical relationship between office workers and common office components that minimize ergonomics risk, including work surface, chair, and computing devices/peripherals
  Distinguish 3 office ergonomics musculoskeletal risk factors relevant to work set up and frequently performed work tasks in a case study scenario
  Propose 2 office ergonomics interventions to reduce risks identified during ergonomic analysis
Learning Objectives

## Slide 12
Follow along with demonstrations unless you think they may cause you a problem
Do not go against doctor's orders or do anything that you feel you should not do
If you are uncomfortable sitting during training, feel move to move
Use your good judgment when trying new techniques or exercises once you complete the training
Workshop Guidelines

## Slide 13
Let’s continue by learning a bit more about you
  Poll – Practice Setting
  Poll – Assessment Experience
  Poll – Ergonomics Consultation
Participant Background/Experience

## Slide 14
Printed Worksheet and PDF Fillable Worksheets
  Printed form completed by filling out form by checking pertinent boxes and writing in comments in each section
  PDF fillable document contains checkboxes and comment fields for each section with option to include pictures
Workstation Assessment Worksheets

## Slide 15
Assist in step-by-step process to conduct office ergonomics assessment
Take Quick Reference Guide with you for first several assessments to help speed up process
Guide offers tips and techniques to enhance assessment effectiveness
Quick Reference Guide

## Slide 16
Pertinent pictures may be included in report
  “A picture is worth a thousand words!”
Valuable teaching tool
  Help individual “see” issues
  Show “before” and “after” pictures
Help supervisor/manager better understand issues/recommendations
Must get approval for pictures
  Person being assessed
  Supervisors, managers, etc.
  Written release may be needed
In some cases, due to proprietary nature of workspace, pictures may not be allowed
A Word about Pictures

## Slide 17
Introducing Michael Wilson
  Works for XYZ Company in Human Resources
  Recently moved into current office
  Would like to ensure appropriate ergonomics set-up and use of workstation
Workshop Case Study

## Slide 18
Assessment notification and scheduling
  Notified of need for assessment
  Contact individual to schedule.
  Typical assessment takes approximately 30 to 45 minutes
Assessment worksheet and equipment
  Assessment worksheets and other equipment (tape measure, camera, sample equipment, etc.) available
Workshop Case Study - Logistics

## Slide 19
Introduction
  If needed, introduce yourself to person being assessed
  Provide background that you are member of Ergonomics Assessment Team
  If person is seated, obtain chair so you can sit with person as you conduct interview and assessment
Workshop Case Study – Conduct Assessment

## Slide 20
Outline assessment objectives:
  Understand pertinent ergonomics related issues
  Conduct step-by-step ergonomics assessment to determine ergonomics issues
  Work with them to "fix" whatever is possible at time of assessment.
  Follow-up available as needed
  Discuss pictures and obtain permission as needed.
  Let them know you will obtain set of measurements
  Ask if they have any questions as you get started with assessment.
Workshop Case Study – Conduct Assessment

## Slide 21
Background information
  Talk with person to complete Background Information section
  Refer to Worksheet
    Fill out form by hand
    PDF fillable form
  Respect confidentiality of information
    Only requesting information specific to ergonomics assessment
Workshop Case Study – Conduct Assessment

## Slide 22
Purpose
  Review with the person the purpose of the assessment
  Improve comfort, safety, and productivity of person in the workplace
  Emphasize 30/30/30 guideline for physical movement
Workshop Case Study – Conduct Assessment

## Slide 23
Observe typical work routine
  Perform typical work tasks
    Perform purposeful work
    Watch for a few minutes
    Perform specific activities they expressed concern about or that you have additional questions about
    Take pictures as appropriate
    Ask them to "freeze" position so you can obtain the desired pictures
  Next step
    Go through step-by-step assessment
    Fill out worksheet
Workshop Case Study – Conduct Assessment

## Slide 24
Workshop Case Study – Observations

## Slide 25
Workshop Case Study – Observations

## Slide 26
Workshop Case Study – Observations

## Slide 27
Anybody remember typewriters?
  Still see one every once in a while
Where do we use computers?
EVERYWHERE!
Typewriters to computers!

## Slide 28
User – Single/Multi
Tasks – Single /Multi
Floor space
Chair
Worksurface
Floor surface
Computer equipment
Telephone
Office equipment
Storage
Conference tables/chairs
Light
Office Components

## Slide 29
Less influenced by need for adjustability of workstation itself
Once determine proper height of worksurface
  Use fixed height or adjustable/fixed worksurface
  Worksurface may be height adjustable
  But once adjusted not readily changed
Single-user

## Slide 30
Multi-user workstations require significantly greater degree of adjustability
  Critical that changeover from one user to next accomplished quickly and easily
Adjustable/adjustable worksurface
  Through spring balanced manual system/powered system worksurface height readjusted within seconds
Multi-user

## Slide 31
Majority of work time accomplishing specific focused task
  For example, customer service representative majority of day on computer and telephone performing computer lookup activities
  Physically job demands are concentrated in single area
Efficient set up is critical because user tends to maintain sustained position to perform activities
Single-task

## Slide 32
Number of different tasks need to be accomplished
  Computer
  Telephone
  Writing workstation
  Attending meetings
  And so on
Does not stay in a sustained position for long periods
Multi-task

## Slide 33
Get general sense of work activity in terms of exposure
  Computer
  Telephone
  Read
  Write
  Meetings
  Misc
  Other
Guides assessment
  What activities to focus on
Work Activity

## Slide 34
In ideal world, dimensions of office workstation
Determined exclusively by job tasks
  Some very focused single-task workstations may be 36 sq ft
  Multitask workstation 120 sq ft or even more
Floor Space

## Slide 35
Floor space may be determined by host of factors not relative to job task
Does not negate need to perform an effective job analysis to make recommendations
Does cause us in many cases to be quite creative!
We do not Live in an Ideal World

## Slide 36
Objectives of chair
  Support body and limbs to provide relief from weight bearing
  Provide stable base or platform for body and limbs
  Position user at correct height and reach relationship to worksurface and tasks at hand
  Allow for easy change in position/movement of user
Chair

## Slide 37
Number of seating systems available in workplace
  Office chairs
  Stools
  Lean platforms
  Other miscellaneous seating
Types of Seating Systems

## Slide 38
Type, use and efficiency of chair are critical elements
Acceptable chair criteria determined by:
  Type of job activities performed
  Size and shape of user
  Duration of time spent in chair
Chair Criteria

## Slide 39
Does the chair have at least 5 legs?
Does the chair roll easily on the floor surface?
  Hard caster on soft floor
  Soft caster on hard floor
Legs and Casters

## Slide 40
Does the chair’s seatpan height adjust up and down?
Seatpan – Height

## Slide 41
Does the chair’s seatpan tilt up and down?
Seatpan – Tilt

## Slide 42
Can you adjust the seatpan tension?
Seatpan – Tension

## Slide 43
Does the chair’s seat slide/move forward or backward?
Seatpan – Depth

## Slide 44
Does the chair fit the individual?
  This gentleman is 7’ tall!
  Arrows point to back of knee and front edge of seatpan
Relationships

## Slide 45
Does chair’s back support move up and down?
Back Support – Height

## Slide 46
Does chair’s back support angle forward or backward?
Back Support – Angle

## Slide 47
Suitable cushion
  Foam density
  Wearability
  Breathability
  Type of material (fabric or rubberized)
Cushion

## Slide 48
Do chair’s armrests adjust
  Up and down
  Side-to-side
  Rotate
Armrests Adjust

## Slide 49
Adjustment levers/knobs/controls
Easy to reach
Easy to manipulate
Should not intimidate

## Slide 50
Therapeutically, exercise balls used in clinical settings as treatment modalities
  Improve spinal stability
Over past several years, use of exercise balls in place of or in addition to task chairs
  Currently only anecdotal evidence exists to support full-time use
Most ergonomists advocate for properly sized/properly adjusted office task chairs rather than use of fulltime ball chairs
Ball Chairs?

## Slide 51
30/30/30 Rule of Physical Movement
  Physically active micro-breaks 30 seconds in length
  Taken about every 30 minutes
  Practiced for next 30 days to make it a habit
Benefits
  Reduce tissue compression and joint stiffness
  Enhance circulation
  Improve overall comfort levels
Encourage person to figure out reminders that work for them
  Post-it notes
  Buddy approach
  Drink a lot of water
  Set reminders on their calendar
Micro-breaks

## Slide 52
Body not designed to sit
  Particularly for long periods
  Studies determined even when seated in well-supported postures
  How soon do we want to move?
  About every 20 to 30 minutes!
Art of Sitting

## Slide 53
Three-point contact
  Sacrum/Trunk
  Hips/Thighs
  Feet/Floor
The Art of Sitting

## Slide 54
90/90 seated posture?
  Only in drawings!
  Most people will sit at 95 to 110 degrees at hips and knees
The Art of Sitting

## Slide 55
Sitting styles quite varied from person to person:
  Percher
  Slouch
  Sit crossed leg
  Sit on leg
Sitting styles

## Slide 56
Particular sitting style needs to be assessed
  Habit developed over time
  Response to poor workstation setup
  Combination of both
What drives problem is frequency and duration of seated position
Sitting styles

## Slide 57
Provide for several different acceptable postures
Rotate throughout day on regular basis
  Upright “keyboard” position
  Semi-reclined/rocking “conversation” position
  Standing
Functional seated positions

## Slide 58
Chairs can be pretty expensive
  All kinds of bells and whistles
  Chair only as good as how it is adjusted
Some people have never adjusted their chair
  Just sit down and go to work!
Bottom line
  Need to initially be able to adjust chair to fit
  As well as throughout day
Adjustment anxiety

## Slide 59
Is chair functioning properly?
No maintenance problems?
Maintenance

## Slide 60
Manual (hardcopy/online)
  Find and read it!
Position and support body/limbs in neutral
  Adjust seat pan/back support tension to hold body in neutral position
  Adjust seatpan height to get feet on floor with even pressure on hips and thighs
  Adjust height and angle of back support to fill in low back curve
  Adjust armrests to provide arm support
Chair Adjustment

## Slide 61
Chair – Case Study

## Slide 62
Chair adjusted with instructions in
  Upright “keyboard position”
  Semi-reclined “conversation position”
Chair – Case Study

## Slide 63
Remember, no matter how perfectly adjust chair to fit
  Still comes down to fact that need to move on regular basis to keep body healthy and safe
Movement is critical to the health of the body!
MOVE!

## Slide 64
Worksurface objectives
  Provide functional workspace (depth, width)
  Support and position equipment
  Provide access to work materials
  Achieve desired relationship match between user/work
Worksurface

## Slide 65
Straight in-line configuration
  Suited for single task activities
  Minimal reach requirements for other office equipment and materials
Straight line (desk/table)

## Slide 66
L-shaped configuration
  Suited for single to multitask activities
Require two or more separate workspaces
  One workspace may be used as computer workstation
  Another as writing or collating workstation
L/U-shape (two/three worksurfaces)

## Slide 67
Corner/cockpit configuration
  Suited for multitask activities in same workspace
  Significant requirements to frequently reach other office equipment and materials
Allows for greatest degree of adjustability and accommodation for user
Corner/cockpit

## Slide 68
Traditional desk at fixed worksurface height of 29 inches
  Millions of these!
  Not designed to be changed in height or angle
  Generally possible to raise fixed height worksurface on supports
  Generally, very difficult to lower it
Worksurface Fixed

## Slide 69
Wall panel mounted worksurface or worksurface on legs
  Can be adjusted within given range
  Once adjusted fixed in that position on fairly permanent basis
Worksurface Fixed/Adjustable

## Slide 70
Sit/stand workstations
  Controlled by mechanical springs or powered mechanisms
Keyboard trays
  User can readily and easily adjust worksurface
Adjustable/adjustable

## Slide 71
Proper work height in relation to worksurface edge
  Many times, will eliminate the issue
Pad sharp edge
  If cannot eliminate pad the edge
Sharp Edges

## Slide 72
Includes organization and structure of tasks/activities performed throughout workday
  Do not store file boxes on the floor!
Work Organization

## Slide 73
House cleaning
Other worksurfaces available for use
  File cabinet at standing height to review documents
Relocate some of equipment on desk
Pullout drawers already in desk
Not Enough Layout Space

## Slide 74
Space in most companies is premium
  Store infrequently used items outside of immediate work environment
Pick up at end of day
Work Organization Solutions

## Slide 75
If work height is adjustable, adjust it as needed
  Raise height of work surface by putting it up on blocks
  Make sure desk or work surface is solidly placed on blocks and won’t fall off!
Adjust chair height
  Make sure feet are supported either on floor or with footrest
Add height/angle adjustable keyboard tray
  Mounted underneath work surface
Worksurface Height Solutions

## Slide 76
Worksurface at standing height
  Stool
  Footrest
Sit/Stand Workstations

## Slide 77
Portable system placed on desk
  Adjustable keyboard/ mouse and monitors
  Use chair when seated
Sit/Stand Workstations

## Slide 78
Height adjustable sit/stand workstation
Sit/Stand Workstations

## Slide 79
Correct worksurface heights
  Seated and standing
Good footwear
  Good walking shoes make for good standing shoes
Anti-fatigue foot mat
  May be beneficial
  Difficult to roll chairs on mats
Footrest/shift weight
  Allows for alternating posture with one foot up and then the other and shifts weight on the feet
Accommodation to sit/stand routine
  Start with specific schedule for first week
  30-minute stand – 30 to 60 second walk – 30 minute seated - 30 to 60 second walk and repeat
  Modify based on unique response
  Remember the mantra: “Don’t wait until it’s too late!”
Tips for Sit/Stand Workstations

## Slide 80
How to enhance audience reception of information
Lack of physical movement is a concern
Conference Rooms
80

## Slide 81
Look for as many opportunities as possible to move as part of meeting
  Standing mixed in with sitting
  Bring in small footrest or back cushion
  Get rid of seated desks
    Meetings will get shorter and perhaps more productive!
Conference Rooms

## Slide 82
Worksurface – Case Study

## Slide 83
In an ideal world the best foot support when seated in a chair is the floor . . .
Never OK to have feet dangling for extended time!
However, if needed use proper sized footrest
Foot Support

## Slide 84
Move what is not needed to some other storage position or get rid of it
Survey work area and determine what is blocking access
  Pencil drawer
  Other
Knee/Foot Clearance

## Slide 85
Foot Support/Clearance

## Slide 86
Computer equipment

## Slide 87
Keyboard configurations
  Straight-line
  Curved
  Articulated
Features
  Keyboard surface finish
  Keyboard size
  Keyboard activation pressure
  Layout
  Wireless
Keyboards

## Slide 88
To use or not to use . . .
  That is the question!
Can be a good addition to a keyboard
  Called a wrist ‘rest’ not wrist ‘anchor’
  Provide some weight-bearing supports for arms to provide opportunity for rest
  Wrists should NOT be anchored to rest when keying
  Move hands and fingers side to side when keying
Keyboard Wrist Rests

## Slide 89
Keyboard shortcut challenge
  Identify common uses for mouse
  Learn keyboard shortcuts instead
  Improve efficiency
Keyboard Shortcuts

## Slide 90
Free float piano playing style
Worksurface forearm support
Keyboard Technique

## Slide 91
Fixed worksurface height
  Use chair seatpan height adjustment to position hands at appropriate position
  Based on technique
    “Piano Player”
    “Forearm Supporter”
  Evaluate foot placement
    Determine if footrest required
    With taller individuals, may need to determine if worksurface can be raised
Worksurface Height Strategy

## Slide 92
Adjustable worksurface height
  Adjust chair’s seatpan height so hips slightly higher or equal to knees and feet supported on floor
  “Piano Player” keyboard user
    Position hands where they would be when using keyboard
    Adjust worksurface height to match hand position
  “Forearm Supporter” keyboard user
    Position hands and forearms where they would be when using keyboard
    Adjust worksurface height to match this position
Worksurface Height Strategy

## Slide 93
Fixed/Adjustable worksurface height
  No access to adjustable sit/stand workstation
    Adjust chair appropriately with feet on floor
    Locate specific point on chair and take vertical measurement from that point to floor
    Have person adjust chair seatpan height to place hands on fixed height keyboard using identified keyboard technique
    Using same point on chair take second measurement to floor
    Difference between two measurements is how much current worksurface height needs to be changed
    Example: initial worksurface height is 29”, difference in two chair measurements was 2”, current worksurface lowered by 2” to 27”
Worksurface Height Strategy

## Slide 94
Fixed/Adjustable worksurface height
  Access to adjustable sit/stand workstation
  Use workstation to figure out recommended heights
    With chair properly adjusted
    Set demo worksurface height
    Take measurements from floor to top of worksurface
    Set actual worksurface to this height
Worksurface Height Strategy

## Slide 95
Stand comfortably tall
  Not forced erect tall but not slumped either
“Piano Player”
  Position hands as if using keyboard
  Adjust worksurface height
“Forearm Supporter”
  Position hands and forearms appropriately
  Adjust worksurface height
Standing Worksurface Height Strategy

## Slide 96
If technique needs improvement
  Back space and delete most commonly used keys?
Training programs teach improved technique
Going from 20 words/minute to 40 words/minute
  100% improvement
  Makes a huge difference in productivity
Poor Technique

## Slide 97
Add stretching to day
  A little post it note put on computer monitor
  Software that reminds you to stretch
  Old-fashioned egg timer
  New-fashioned FitBit
  Team up with someone else in office
  Take advantage of natural breaks between activities
  Drink lots of water!
Take break
Remember to Stretch!

## Slide 98
Keyboard – Case Study

## Slide 99
Response to first personal computers
Keyboard tray configurations
  Keyboard tray size
  Keyboard/mouse
  Height/angle adjustment
  Knee clearance
Keyboard Trays

## Slide 100
Keyboard Tray – Case Study

## Slide 101
No not that kind of mouse!
Use mouse as little as possible
  Keyboard shortcuts
  Productivity improvement
  Less need to reposition hand on mouse from keyboard
Mouse

## Slide 102
Neutral positions
  Same plane as keyboard
Mouse placement
  Free float piano playing style
  Use of worksurface for forearm support
Right or left-hand use
  May consider switch from one hand to the other
  Reduce exposure of only one hand using mouse
  Works for some not for all people
Mouse technique

## Slide 103
Pointing Device Non-neutral Positions

## Slide 104
Mouse Setup
  Buttons
    Swap sides
  Pointers
  Pointer Options
    Pointer speed
    Snap To
    Show location with CTRL key
  Wheel
    Change scroll rate
  Hardware
Mouse Set-up

## Slide 105
In most cases, mouse wrist rest is not recommended
  Wrist rest tends to “anchor” wrist
  Excessive side-to-side deviation of hand
Straight in access
  Allow forearm, wrist and hand moving as unit to manipulate mouse
  Think of mouse as extension of arm NOT just extension of wrist
Mouse Wrist Rests

## Slide 106
Mouse Types

## Slide 107
Mouse – Case Study

## Slide 108
Where?
  Computer underneath monitor
  May or may not be appropriate
  Don’t block ventilation
  On/off and disc drives access
Laptop/Desktop

## Slide 109
Design violates basic ergonomic principles
Fixed position keyboard and monitor
Laptops

## Slide 110
Occasional Users
  Better off sacrificing neck posture rather than wrist posture
Find comfortable chair
  Position in lap or on table for most neutral wrist posture that you can achieve
  Angle laptop screen so can see with least amount of neck deviation
Occasional Laptop User

## Slide 111
Use separate keyboard/mouse
  Port replicator/docking station
Position on desk/worksurface to see screen without bending neck
  Elevate off desk surface using stable support surface, such as computer monitor pedestal
  Follow postural guidelines for working at computer workstation
Transport with bag or wheeled cart
Full-time Laptop User

## Slide 112
Laptop/Decktop – Case Study

## Slide 113
Everything need access to may be viewed through monitor
Watch people looking at their monitors
  Almost like monitor is a vacuum cleaner
  They turn it on . . . and it sucks their head right in!
  The “Thinker” Pose!
Monitor

## Slide 114
Where do we naturally read?
We read by looking out and down
Monitor Height

## Slide 115
Top of screen no higher than eye level
Look out and use downward eye movement to look at lower part of screen
Monitor Height

## Slide 116
If screen too high
  Forces eyes wider open than usual
  Less tearing - eyes become more dry
  Tip head back putting additional strain into neck and shoulders
Solutions
  Lower monitor
  Tip monitor slightly forward
  Raise chair slightly
  Lower worksurface slightly
Monitor Too High

## Slide 117
If screen too low
  Head forward
Solutions
  Adjust monitor stand – if adjustable
  Monitor arms
  Monitor stands/Risers
Monitor Too Low

## Slide 118
Eyes
  Accommodation
  Convergence
Guideline
  Get screen as far away from user as possible
    At least arm’s length
    Still be able to read it clearly with good posture
Monitor Distance

## Slide 119
Slide screen towards user
  On worksurface
  Monitor arm
Monitor Too Far Away

## Slide 120
Reconfigure monitor placement on desk
Add keyboard tray
At minimum push chair back from worksurface to give eyes a break
Monitor Too Close

## Slide 121
Directly face primary work task
  Primarily data creation or manipulation
    Monitor directly in front
  Primarily data entry - main focus on paper documents
    Monitor slightly off to side
    Copy stand to place paper documents directly in front
Monitor Alignment

## Slide 122
Primary/Primary
  About 50% each monitor
  Middle of two monitors
  Centered on user’s nose
  Equal head rotation from side-to-side
Dual Monitors

## Slide 123
Primary/Secondary
  Primary monitor viewed primarily
    60 to 90% of the time
    User centered on Primary
  Secondary monitor viewed occasionally
    10 to 40 % of the time
  Limit asymmetrical head/neck position
Dual Monitors

## Slide 124
Pixel (picture element)
  640 by 480
  800 by 600
  1024 by 768
  1600 by 1800
Guideline
  Set LCD monitor resolution to native resolution
  Typically, the highest it will go
  Consult with IT if needed
Monitor Resolution

## Slide 125
Close eyes and position head in balanced neutral position on neck
Open eyes
  With proper monitor height
  View top third of screen without any head movement
  View bottom third of screen
  Look for downward eye movement of up to 30 to 40 degrees and perhaps a small amount of head down tip
Make any monitor position changes indicated
Functional Monitor Placement Test

## Slide 126
Unwanted light directed or reflected into eyes
Sources
  Overhead lights
  Task lights
  Outside light
  Any shiny surface
  Any white/bright object
Glare

## Slide 127
First step
  Identify glare source
    Windows
    Lights
    Floor
    Etc.
Control
  Control source
    Window shades
    Light direction
  Control path
    Repostion monitor
Control Glare

## Slide 128
Get what you pay for
  Inexpensive glare screen is generally just wire mesh
  Will cut glare at expense of character quality
  Good quality optical glass glare screen
Don’t have light source such as window directly behind monitor
  Reposition monitor
  Shade window
Use glare screen

## Slide 129
Check if brightness and contrast can be adjusted
  Adjust based on user’s perception of overall quantity and quality of light
Adjust Monitor Screen Brightness/ Contrast

## Slide 130
On regular basis clean monitor screen
Only use approved cleaning measures
Clean Monitor

## Slide 131
Regular eye examinations
Eyewear prescriptions changes
Eye health in general
Based on job task
Eye Examinations

## Slide 132
Age-related process
Slow loss of flexibility within lens inside eye
  Inability to focus at closer distances
  With bifocals may result in head tip
Solutions
  Computer glasses
  Lower monitor
Presbyopia

## Slide 133
Monitor – Case Study

## Slide 134
Head position
  Horizontal vs. inclined
  What does your head weigh?
Out-of-neutral head position increases neck and shoulder strain
Document Holder

## Slide 135
Landscape
Portrait
Read Write Stand
Document Holders

## Slide 136
Document Holder

## Slide 137
Frequency and duration
  More than 1 to 2 hours/day
  More than 1 to 2 minute calls
  Should consider use of hands free to operate equipment
Telephone

## Slide 138
Handsets
  Awkward head, neck and arm position
Shoulder cradle
  Still have awkward head, neck and arm position
Telephone Types

## Slide 139
Headsets
  Wireless
  Bluetooth
Telephone Types

## Slide 140
Telephone

## Slide 141
Make use of principles to position office equipment
  Calculator
  Printer
  Fax
  Writing utensils
  Scissors
  Paper clips
  Stapler
  Stuff
Office Equipment

## Slide 142
Relationships

## Slide 143
Primary
  Frequently accessed from seating system
  Within easy reach
Secondary
  Occasionally accessed
  Located in gray zone
  Danger Zone!
Tertiary
  Very occasionally accessed
  Have to get up and move to access
Storage

## Slide 144
Storage types
  Vertical storage racks
  Horizontal storage bin
  Wall hanging storage
File cabinet types
  Vertical
  Lateral
  Rolling
Don’t overfill
  50 files in cabinet that holds 30!
Storage

## Slide 145
Storage

## Slide 146
Illumination – Ambient and Task

## Slide 147
Too much
  Turn out lights
Too little
  Add overhead lights
    Add indirect lights
    Bounce light off of ceiling and walls
  Add task light
    Desktop or wall panel lamp
    Position light carefully
Lighting Design
  Consult with the building Facilities group
Ambient Light Solutions

## Slide 148
Task lights
  Desktop or wall panel lamp
  Position light carefully
  Reading material
Task Light Solutions

## Slide 149
Illumination

## Slide 150
Recommended Specifications – Case Study

## Slide 151
Assessment Follow-up – Case Study

## Slide 152
Sample Assessnent Reports

## Slide 153
Great number of factors enter into the office ergonomics workplace
Use the principles and ergonomics analysis process to offer solutions that are practical and effective!
Ergonomics – A Potent Tool!

## Slide 154: Thanks for your Time and Attention!

## Slide 155: WorkWell Prevention and Care and ErgoSystems Present
Office Ergonomics: Introduction for Health Care Professionals (Online)
WorkWell Prevention and Care
ErgoSystems Consulting Group, Inc.
MENU

## Slide 156
Mark A. Anderson, MA, PT, CPE
  Mark Anderson, MA, PT, CPE is the president and founder of Minneapolis, Minnesota based ErgoSystems Consulting Group, Inc. Anderson started working clinically in the Industrial Rehabilitation arena in the mid 1980’s; this led to his interest in ergonomics. Since 1993, he has been certified by the Board of Certification in Professional Ergonomics as a Certified Professional Ergonomist (www.bcpe.com).
  Anderson is a graduate of the University of North Dakota Physical Therapy program and holds a Master of Arts degree in Physical Therapy from the University of Iowa. He has consulted in ergonomics for over 30 years.
  Anderson has worked with WorkWell since 2005 developing the current Office and Manufacturing Ergonomics training courses. An experienced consultant and instructor, he has developed and implemented ergonomics consultation and training strategies for a wide range of companies, organizations and local, state and federal government agencies. Including Emerson Process Management, Tescom, Tennant Company, General Electric, Alliant Techsystems, Boston Scientific Corporation, Quaker Oats, Pepsi-Cola, General Mills, Medtronic, Fingerhut, Panama Canal Commission, United States Navy and Marine Corps, United States Customs Service, Social Security Administration, USDA Animal and Plant Health Inspection Service and state and local governments.
  Anderson has written a number of publications and spoken nationally and internationally on ergonomics. He has been active in the Upper Midwest Chapter of the Human Factors and Ergonomics Society serving as the past secretary and co-program chair.
Course Developer

## Slide 157
Kristen Cederlind, OTR/L
  Kristen Cederlind, OTR/L joined the WorkWell team in 2013, first serving as a Manager of On-Site Services and more recently, assuming the role of Director of the WorkWell Quality Provider Network.
  With over 25 years of experience as an Occupational Therapist, she has consulted with manufacturing employers across the country to develop customized On-Site therapy and wellness programs to improve employee health and safety, while collaborating with the rest of the On-Site team in service implementation, provider training, customer and provider relations and metrics reporting.
  Her background includes program development and management of a hospital acute care and outpatient rehabilitation department. Her partnership with WorkWell began in 2003, when the hospital joined the WQP network and received training in FCE, FJA and PWS programs.
  While working in the hospital setting, she championed ergonomics initiatives such as safe patient handling and office ergonomics and was able to utilize job analysis and prework screening skills both within the hospital and in her local community.
  Kristen is a graduate of the University of Southern California and is a member of both the California and American Occupational Therapy Associations.
Faculty

## Slide 158
Dee Daley, PT, DPT
  Dee Daley, PT, DPT is a graduate of the University of North Carolina- Chapel Hill and Quinnipiac College physical therapy programs. Dee is currently employed by WorkWell in New Ipswich, NH as Director of Clinical Practice.
  Dee has been a member of the WorkWell faculty since 2003, and intermittently teaches as a guest lecturer for PT and PTA schools on topics related to Work Injury Prevention and Management. Dee also holds a degree in Health Professions Education from North Carolina State University.
  In addition to clinical practice, Dee has been active in the New Hampshire and North Carolina Chapters of the American Physical Therapy Association (APTA) as President and other roles in the area of Education and Policy.
  In addition to helping develop training materials for WorkWell, she has coauthored several publications on the Role of PT in Occupational Health and Wellness, and Safety in Functional testing.
  She has also served as a member of the APTA as a working member of the Occupational Health Special Interest Group and Work Rehab Clinical Practice Guideline group
Faculty

## Slide 159
Robin Peterson, PT
  Robin Peterson PT is a graduate of the University of Minnesota Physical Therapy Program. Robin is currently employed by Regions Hospital in St. Paul MN as Physical Therapist and Supervisor.
  Robin has been a faculty member and consultant for WorkWell since 2008. Robin also holds a Bachelor of Arts degree in Distributive Sciences and Psychology from Gustavus Adolphus College in St. Peter MN.
  In addition to clinical practice and consulting, Robin Peterson has been an active member in the MN chapter of the APTA since 1987 and has served as the physical therapy alternate member for the MN Medical Services Review Board with the Department of Labor and Industry since 2002.
  Robin Peterson is also a member of the National Association of Occupational Health Providers and Human Factor Society.
  She co-authored Smart Tracks patient management system, Volumes I and II.
Faculty

## Slide 160
Marc Yeager, PT, MPT
  Marc Yeager, MPT, is a graduate of Loma Linda University, where he received a bachelor’s degree in Life Sciences and a Master of Physical Therapy degree in June 1993. Marc is the Managing Principal of Injury Prevention & Management Consulting.
  Marc has been a member of the American Physical Therapy Association since 1994 and the Georgia Physical Therapy Association since 1997. He has been a faculty member for WorkWell Systems since 2006. He achieved the distinction of WorkWell Master Clinician in 2001 with certifications in Functional Capacity Evaluations, Functional Job Analysis, Return to Work Clinical Pathways, Functional and Office Ergonomics.
  Marc founded Highland Park Physical Therapy in 2001, shortly before joining WorkWell Systems as an Occupational Health Specialist developing injury prevention and management programs, including Rapid Return to Work, Stress Factor Analysis, and supportive training materials, in addition to implementing internet-based injury prevention and management programs for industrial clients.
  Marc has assisted in the development and implementation of on-site ergonomic programs for a Silicon Valley-based high-tech Fortune 100 Company and served as a member on their ergonomic safety committee as an external consultant.
Faculty

## Slide 161
Title Slide
Welcome
Objectives/Guidelines
Worksheet/Reference Guide
Case Study – Introduction
Office Components
Chair
Worksurface
Sit/Stand Workstation
Foot Support/Clearance
Keyboards
Trays
Mouse
Laptop/Desktop
Monitors
Document Holder
Telephone
Storage
Illumination
Recommended Specifications
Sample Reports
Summary/Close
Resources
Faculty
Menu
Menu

## Slide 162
Topics
  Successful office workplace
  Office Ergonomics Evaluation Worksheets – Introduction
  Office Ergonomics – Case Study Introduction
  Typical office components - review
  Office ergonomics evaluation (worksheet review)
  Recommended Specifications
  Sample Office Ergonomics Assessments
  Summary and Close
Downloadable Handouts and Forms
  Workstation Evaluation Worksheets (fillable pdf)
  Office Ergonomics Quick Reference Guide (pdf)
  Common Keyboard Shortcuts
  Post Course Online Assessment (link sent following training)
Schedule 10 min. break mid way through class - at faculty discretion

## Slide 163
Evaluation Worksheets
  Office Ergonomics Workstation Assessment Worksheet PDF Fillable Template with Pictures
  Office Ergonomics Workstation Assessment Worksheet PDF Fillable Template without Pictures
  Office Ergonomics Workstation Assessment Worksheet PDF Manual Entry
Quick Reference Guide
  Office Ergonomics Assessment Quick Reference Guide (PDF)
Manual
  Office Ergonomics Training Manual (PDF)
Case Study – Example Reports
  Ergonomics Workstation Assessment Worksheet Example 1
  Ergonomics Workstation Assessment Worksheet Example 2
  Ergonomics Workstation Assessment Worksheet Example 3
Resources